## Slide 1: Routing and Wavelength Assignment Information Encoding for Wavelength Switched Optical Networks draft-ietf-ccamp-rwa-wson-encode-13.txt
Greg M. Bernstein (ed.), Grotto Networking
Young Lee (ed.), Huawei
Dan Li, Huawei
Wataru Imajuku, NTT
Jianrui Han, Huawei
Diego Caviglia, Ericsson
Anders Gavler, Acreo
Jonas Martensson, Acreo
Itaru Nishioka, NEC
Cyril Margaria, NSN

## Slide 2: Updates from v.11 to v.12
Added clarifying text on Resources, Blocks, Sets, and the Resource Pool (In Section 3)
Added clarifying text on RB and RB Set in Section 3.1.
“In a WSON node that includes resource blocks (RB), denoting subsets of these blocks allows one to efficiently describe common properties of the blocks and to describe the structure and characteristics, if non- trivial, of the resource pool. The RB Set field is defined in a similar manner to the label set concept of [RFC3471].”

## Slide 3: Resources, Blocks, Sets and Pool
Simple hierarchy:
  The resource pool is partitioned into resource blocks containing individual resources.
Efficient and general encoding:
  Resources blocks are combined into sets for encoding of common properties.
R = resource
RB = resource block
RB sets:
(RB1, RB2),
(RB2, RB3, RB4),
Etc…
RBp
R
R
RB1
R
R
R
…
RB2
R
R
R
R
Resource Pool

## Slide 4: Updates from v.12 to v.13
Editorials.
3.1. Resource Block Set Field
  16 bit RB Identifier -> 32 bit RB Identifier
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action |C| Reserved | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Identifier 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: : :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Identifier n |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Updated the examples in appendix to reflect this change.

## Slide 5: Next Steps
Ready for WG LC 