## Slide 1: GMPLS OSPF Enhancement for Signal and Network Element Compatibility for Wavelength Switched Optical Networks draft-ietf-ccamp-wson-signal-compatibility-ospf-07.txt
Young Lee (ed.), Huawei
Greg M. Bernstein (ed.), Grotto Networking

## Slide 2: Updates from previous versions
Section 2: Added the following clarifying text:
  [RFC3630] defines OSPF TE LSA using an opaque LSA. This document adds a new top level TLV for use in the OSPF TE LSA: the Optical Node Property TLV.
  The Optical Node property TLV describes a single node. It is constructed of a set of sub-TLVs. There are no ordering requirements for the sub-TLVs. Only one Optical Node TLV shall be advertised in each LSA.
  All sub-TLVs defined here may occur at most once in any given Optical Node TLV.
    Resource Block Information Sub-TLV
    Resource Pool Accessibility Sub-TLV
    Resource Block Wavelength Constraints Sub-TLV
    Resource Pool State Sub-TLV
    Block Shared Access Wavelength Availability Sub-TLV
  "At most once" means that if there is sub-TLV related information, it should be always included. These restrictions need not apply to future sub-TLVs. Unrecognized sub-TLVs are ignored.

## Slide 3: Updates from previous versions
Added a new Section 3 To discuss Scalability and Timeliness
  Current Optical Node Property TLV encodes the following list of sub-TLVs:
  In a rare case where the LSA exceeds the IP MTU limit, then the draft only allows the following sub-division rule (Section 3.1):
    Each sub-TLV will be packaged as the sole element in an OSPF TE LSA with a unique Link State ID.
Added text to explain dependency among sub-TLVs and an implication of late or missing sub-TLVs.

## Slide 4: Sub-Division Rules (Illustrations)
OSPF TE LSA (LSA ID = ‘A’)
Optical Node Property TLV
Resource Block Information Sub-TLV
Resource Pool Accessibility Sub-TLV
Resource Block Wavelength Constraints Sub-TLV
Resource Pool State Sub-TLV
Block Shared Access Wavelength Availability Sub-TLV
OSPF TE LSA (LSA ID= ‘B’)
Optical Node Property TLV
Resource Block Information Sub-TLV
OSPF TE LSA (LSA ID= ‘C’)
Optical Node Property TLV
Resource Pool Accessibility Sub-TLV
OSPF TE LSA (LSA ID= ‘D’)
Optical Node Property TLV
Resource Block Wavelength Constraints Sub-TLV
OSPF TE LSA (LSA ID = ‘F’)
Optical Node Property TLV
Block Shared Access Wavelength Availability Sub-TLV
OSPF TE LSA (LSA ID= ‘E’)
Optical Node Property TLV
Resource Block Wavelength Constraints Sub-TLV

## Slide 5: Next Steps
Revise document per WG mailing agreement by removing section 3.2 and then Ready for WG LC 