## Slide 1: Usage of The RSVP Association Object draft-ietf-ccamp-assoc-ext-01
Lou Berger <lberger@labn.net>
Francois Le Faucheur <flefauch@cisco.com>
Ashok Narayanan <ashokn@cisco.com>

## Slide 2: Updated based on comments made at last IETF
Comment:
TP –identifiers, RFC6370, dropped ICC
  ICC moved to new draft
    draft-ietf-mpls-tp-itu-t-identifiers
    Draft currently has an ICC_Operator_ID
      Composed of two character Country Code (CC) followed by a six character ITU Carrier Code (ICC)
    Future of this draft is unclear

## Slide 3: draft-ietf-ccamp-assoc-ext-01
Aligned with RFC6370
  Drops all references to ICC
    Was carried in the Extended Association ID
Is ICC_Operator_ID “ready”
  Can carry CC:ICC, if ICC_Operator_ID draft moves forward
Format:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Length | Class-Num(199)| C-Type (TBA) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Association Type | Association ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IPv4 Association Source |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Global Association Source |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: . :
: Extended Association ID :
: . :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Global ID: <0> |
<2|4-byte ASN>
[<CC><ICC>] [<data>]
Per RFC 4872
>= 0 bytes,
32-bit
aligned
4 bytes

## Slide 4: Next steps
Agree on approach for supporting draft-ietf-mpls-tp-itu-t-identifiers / ICC_Operator_ID
  Option 1: Keep as is -- ICC_Operator_ID “ready”
    Ready for WG LC, if follow this approach
  Option 2: Add text related to ICC_Operator_ID
    Publication of RFC will be gated by mpls-tp-itu-t-identifiers
Comments?