## Slide 1: Options to Transport CLUE Messages draft-wenger-clue-transport-01
<number>
Stephan Wenger Roni Even
Gonzalo Caramillo
Marshall Eubanks

## Slide 2: Constraints
<number>
SIP to be used as base protocol for call setup
  Charter, backward compatibility
“Framework” draft requires (for valid reasons) handshake different from what is commonly used in SIP
  (offer/answer (OA) vs. three-trip handshake)
Unclear whether there is conceptual difference between “initial” CLUE information, and CLUE information exchanged during the lifetime of a session. Suspicion: no significant difference

## Slide 3: Conclusion #1
<number>
Need two stage “negotiation”: first SIP, then CLUE
  Can probably overlap at least partially

## Slide 4: Options for transporting CLUE exchange
<number>
Piggy-backing on SIP (SIP-INFO, SIP-UPDATE, RE-INVITE)
  Preference for SIP-INFO over other SIP methods expressed on mailing list
  Package needed
CLUE stream as a SIP-negotiated “media” stream
  Message Session Relay Protocol (MSRP, RFC 4975)
  CLUE-specific framing over some transport
  Other
Content indirection, multi-MIME body, allows non-SDP
  FTP and config files (as TeleSuite did)
  Dismissed as impractical

## Slide 5: Conclusion #2
<number>
Two options:
  CLUE stream as a SIP-negotiated “media” stream
  CLUE messages piggy-backed on SIP using SIP-INFO

## Slide 6: CLUE negotiation over SIP-established “media” stream
<number>
Setup “CLUE” media stream through SIP w/ OA
Assumed OA result: “CLUE” session goes through
CLUE handshake over CLUE “media” stream
Based on results of CLUE handshake, setup of full audiovisual functionality by SIP-UPDATE or SIP-REINVITE
  To re-use existing functionality in codec boxes
  CLUE as a bolt-on

## Slide 7: Options for CLUE “media” stream
<number>
UDP recommended because of NATs, firewalls.
Problem: UDP is unreliable
  Packet size under MTU: no issue, redundant sending, but unlikely given complexity of CLUE
    That’s assuming XML-ish representation. Perhaps can use compression, binary model, …?
  Devise our own BFCP-like handshake using UDP-based transport.
TCP mentioned again as an option (K. Drage, 11/2)
  Can we come to a conclusion that, for our industry, TCP is NOT an option (even with ICE TCP) ?
<number>

## Slide 8: Conclusion #3
<number>
  CLUE WG to devise our own BFCP-like handshake to make CLUE media stream sufficiently reliable

## Slide 9: CLUE message Content Representation
<number>
As suggested, we are NOT constrained to use SDP; modern, flexible formats are OK
XML natural candidate
Is CLUE presentation in XML exceeding UDP MTU? Probably yes, especially for multipoint
  This is independent from the transport over “SIP” or over “SIP-negotiated UDP channel”
  Issue of fragmentation will arise for any format, especially if 1000’s of endpoints can participate in a session.
Issue of congestion control
  Telepresence is supposed high bandwidth media, signaling is drop in a bucket
  Need to support dozens/hundreds of clients, some of which may be behind slow link.
  Conclusion: YES, we need congestion control

## Slide 10: Conclusion #4
<number>
Use XML for CLUE message content representation

## Slide 11: Conclusions Summary
<number>
Need two stage “negotiation”: first SIP, then CLUE
  Can probably overlap at least partially
Two options for transport:
  CLUE stream as a SIP-negotiated “media” stream
  CLUE messages piggy-backed on SIP using SIP-INFO
CLUE WG to devise our own BFCP-like handshake to make CLUE media stream sufficiently reliable
  Certainly for media stream option, but also for SIP-INFO option?
Use XML for CLUE message content representation