## Slide 1: CLUE Points and Areas of Capture
Brian Baldino

## Slide 2: What is this addressing
Enable describing devices in 3-dimensional space
Enable receivers to render correctly in terms of spatial placement
Enable implementers to give a sense of real-world dimensions
Enable multiple viewpoint use cases
Enable complex devices to be described accurately but don’t burden simple devices

## Slide 3: Proposal
Coordinate system is Cartesian X, Y, Z
  Origin (0, 0, 0) located at a spot of the implementer's choosing
Coordinates can either be “virtual” or “real” units (mms).
Each capture set has its own coordinate system, independent of those for other capture sets

## Slide 4: Directionality
Z
Y
X
Right to Left
Low to High
Front to Back
As numbers increase for the X axis, movement is from audience right to audience left
As numbers increase for the Y axis, movement is from audience low to audience high
As numbers increase for the Z axis, movement is from audience front to audience back

## Slide 5: Relevant Terms
For each media capture there is a ‘point of capture’ and ‘area of capture’ defined
  Point of capture is the location from which the media is captured and is defined by a single point
  Area of capture is the extent captured by the media capture and is defined by 4 points

## Slide 6: Point of Capture/Area of Capture
Area of capture,
top left: -1000, 500, 3000
Point of capture: 10, 10, 10
Area of capture,
bottom left: -1000, -500, 3000
Area of capture,
top right: 1000, 500, 3000
Area of capture,
bottom right: 1000, -500, 3000
Notes: Change coordinates of point of capture here

## Slide 8: 3 Camera Example
VC0
VC1
VC2
100,0
0,0
-100,0
-50,120
150,120
Area of capture co-ordinates
Point of capture co-ordinates
(table)
-150,120
50,120
x axis
z axis
Notes: For simplicity, this and further examples take an aerial view of the “room” and so reduce the X,Y,Z co-ordinates to just X and Z. The Y co-ordinate would be 0 for the camera origin, and negative or positive for the camera destination area depending on whether the cameras were pointing upward at the people in the room or downward.
This scenario involves 3 cameras, each of would typically be mounted above the centre of a screen. Each camera looks out at 2 seats of the available 6

## Slide 9: Curved Table Example
VC0
VC1
VC2
100,0
0,0
-100,0
-50,120
150,100
Area of capture co-ordinates
Point of capture co-ordinates
(table)
-150,100
50,120
x axis
z axis

## Slide 10: 2 Camera ‘Crossed’ Example
(table)
VC0
VC1
25,0
-25,0
0,120
-100,120
100,120
Area of capture co-ordinates
Point of capture co-ordinates

## Slide 11: Multiple Viewpoint Example
VC0
VC1
VC2
100,0
0,0
-100,0
100,120
(table)
-100,120
Area of capture co-ordinates
Point of capture co-ordinates
Notes: Slightly simplified diagram
What’s important is that all 3 VCs have the same area of capture.

## Slide 12: Final thoughts
Allows for modeling things like gaps between captures
Providing coordinates for a capture set is optional
  Devices that know their physical dimensions should provide them
  Simple devices need not be burdened