## Slide 1: draft-ietf-codec-results-00
Jan Skoglund, Christian Hoene
November 15th, 2011

## Slide 2: Diff to draft-valin-codec-results-00
Added test results of Google and Universität Tübingen (Section 2.1.4, 2.1.5 and 2.4)
Editorial changes
  Moved Section 2 and 3 to the appendix – as suggested by email comments
  Moved Section 4 to the appendix as it also refers to old implementations.

## Slide 3: Results of Google
Can Opus compress
  tonal languages (in this case Mandarin) well?
What is the impact of transcoding
  with AMR and AMR-WB?
Measurement Methodology
Followed MUSHRA ITU-R BS.1384-1
Headphones

## Slide 8: Results of Universität Tübingen
Can Opus compress
  stereo voice in the Silk and the Hybrid mode?
  two simultaneous voices?
  binaural content?
How does Opus perform compared to other stereo voice codecs?
  No open source stereo voice codec available
  thus, used AMR-WB+
Measurement Methodology
  Followed MUSHRA ITU-R BS.1384-1
  Headphones
  Participants were unaware of a hidden reference

## Slide 9: Reference Items
One Voice Stereo 8s, stereo voice recording, female German speakers
Two Voices Stereo 9s, two stereo female voices mixed together
One Voice Binaural 13s, one female voice, rendered with HTRF and added room impulse response, moving
Two Voice Binaural 13s, two female voices at different stationary positions, rendered with HTRF and added room impulse response
Acappella Song „Mein Fahrrad“ by „Die Prinzen“ 10.5s, mono

## Slide 10: Results: Codecs
CI 95%

## Slide 11: Codec and Item
CI 95%

## Slide 12: Summary of both tests
Encoding of Mandarin works well – Passed
  However, Opus at 20 kbps did not outperformed G.719 at 32 kbps as with English
  Mandarin seems not to contain as much contain as much high frequency-rich consonants as English
Transcoding via AMR and AMR-WB – Passed
  Opus better than AMR-WB
Stereo voice coding in CELT mode – Passed
Stereo voice coding in CELP mode – Fixed?

## Slide 13: Next steps: Codec characterization
Codec characterization needed for
  People selecting codecs
  Application programmers
Work can only be started after code freeze.
Old test results might be use but only after testing output of old version equals output of new version
Shall we run objective tests on speech and audio quality as well as runtime and memory consumption?
Merging with draft-hoene-quality-01 to include some more textual descriptions?

## Slide 14
Please send new listening-test results to the editor (hoene@uni-tuebingen.de)
Thanks…