## Slide 1: DHCPv6 class based prefix (draft-bhandari-dhc-class-based-prefix-00)
IETF 82, November 2011
Authors:
Shwetha Bhandari (Cisco)
Sri Gundavelli(Cisco) Gaurav Halwasia (Cisco) Sindhura Bandi (Cisco),
Hui Deng (China Mobile)

## Slide 2: Motivation/Use cases
Mobile Network
  Mobile gateway as a DHCPv6 PD client and a DHCPv6 Server serving DHCPV6 clients attached to it
  Prefix with different properties. Example: Prefix can be setup for –
    VEHICLE DIAGNOSTICS - This prefix is intended for assigning the addresses to on-board vehicular computers built-in to the automobile. The routing for these prefixes is not beyond the vehicle's manufacturer.
    INTERNET ACCESS FOR END USERS - This prefix is intended for assigning it to the end users in the vehicle for Internet access.
    PREFIX IS FROM LOCAL ACCESS NETWORK, NON-MOBILE PROPERTIES - PREFIX IS FROM LOCAL ACCESS NETWORK, NON-MOBILE PROPERTIES with no mobility supported.
    GLOBAL HOME AGENT ASSIGNED, CHAINED MOBILITY - This prefix is topologically anchored in the mobile node's home network. It has mobility properties.
    MANAGEMENT INTERFACES - This prefix is intended for assigning them to the management interfaces of the network nodes in the vehicle.
    Low latency suitable for Voice applications

## Slide 3
For supporting offload function for certain traffic in chained mobility scenario, the UE needs to use the right source address for the right application flows, based on the offload requirements. The obtained address configuration can be from EPC or from the local domains.
Macro Cell
Access
Wireless LAN
Controller
PDN Gateway
Evolved Packet Core
Wireless LAN Access
802.11 AP
P1::1/128
Micro-Mobility Domain
Internet
Local Internet Offload Point
Home Routed Traffic
App-2
App-1
Address Pool: P1::/48
Address Pool: P2::/48
P2::/128
#1: WLAN-EPC Integrated Architecture

## Slide 4: #2: Home Network Scenarios
Home network
  Evolution of home networks to use IPv6 - IPv6 source address of the hosts used as a parameter for route decision and provide differentiated service for different classes of devices within a home network
  Home gateway – As a DHCPv6 PD client to SP DHCPv6 Server and the DHCPv6 server for devices in home network
  Prefix with different properties. Example Prefix setup for:
    IP Television and Video devices – To enable source based routing of video traffic with it QoS demands
    Guest users – SPs can provide guest users with limited access from home
DHCPv6 Client on the WAN side
Obtains prefixes with different properties.
DHCPv6 Server in LAN network
Home gateway
(Requesting Prefix)
Home gateway
(Serving IA_NA and IA_PD requests)
Video device requests and gets Address from prefix with property “video”
IPv6 smart grid router requests and gets prefix with “sensor-network” property

## Slide 5: Problem Statement
  DHCPv6 Server - can delegate longer prefixes and IA_NA assignments from shorter prefix learnt via DHCPv6 PD (RFC 3633)
    Further delegation of a delegated prefix– DHCPv6 PD client assuming the role of DHCPv6 Server needs to delegate prefix or assign IA_NA based on prefix property.
  DHCPv6 PD Client – Can request for prefix with specific properties
  DHCPv6 IA_NA Client – Can request for IA_NA from a prefix range with specific properties
  DHCPv6 Prefix delegation – DHCPv6 PD provides no semantics to request and associate prefix with specific properties today

## Slide 6: Proposed Extension
New DHCPv6 option to associate Prefix with its properties:
DHCPv6 PD client – To include OPTION_PREFIX_CLASS in DHCPv6 Solicit message
DHCPv6 IA_NA client – To include OPTION_PREFIX_CLASS in DHCPv6 Solicit message
DHCPv6 Server to include OPTION_PREFIX_CLASS in:
  OPTION_IAPREFIX option in Advertise messages for Prefix delegation
  OPTION_IA_NA option in Advertise message for IA_NA assignment

## Slide 7: Next Steps
Authors appreciate feedback from the WG