## Slide 1
Nov.2011
Progress of Relay Agent Encapsulation for DHCPv4
Notes: 整个ppt的色调风格需要统一
<number>

## Slide 2
Status of current version
draft-ietf-dhc-dhcpv4-relay-encapsulation-01
    Define new messages to convey relay agent information: RELAYFORWARD, RELAYREPLY
    Define relay agent behavior, including L2 relay agent and L3 relay agent
    Define DHCP server behavior
    No change on DHCP client behavior

## Slide 3
Brief description of mechanism
client
L2RA
L3RA
server
BOOTREQUEST
BOOTREPLY
RELAYREPLY
RELAYFORWARD
RELAYFORWARD
RELAYREPLY
(1) When DHCP message toward server go through a relay agent, RA encapsulate it into a new message, RELAYFORWARD message, and add its information in at the same time
(2) DHCP server decapsulate RELAYFORWARD message and response a RELAYREPLY message
(3) When RELAYREPLY message go through a relay agent, RA decapsulate it to get the relative RA info and send a new RELAYREPLY message or a normal DHCP message if it’s the closest RA to client

## Slide 4
Implementation of Relay Agent Encapsulation for DHCPv4
We build four hosts in VMware Workstation:
We modify and run isc dhcp-4.2.0 version based on “draft-ietf-dhc-dhcpv4-relay-encapsulation-01” in three hosts for our experiment
  L2RA
    Encapsulate message into a new message
    Add some sub-options into relay segment, such as Circuit ID, Link selection,and SUBOPT_L2AS if the L2RA is close to the client
    Decapsulate RELAYREPLY message
  L3RA
    Encapsulate message into a new message
    Add some sub-options into relay segment, such as Circuit ID, Link selection.
    Decapsulate RELAYREPLY message
  Server
    Decapsulate RELAYFORWARD message
    Construct RELAYREPLY message and send to relay agent
server
client
L2RA
L3RA

## Slide 5
Implementation of Relay Agent Encapsulation for DHCPv4
Experiment result (1)
L2RA constructs the RELAYFORWARD message by adding fixed-length header and relay segment.
Fixed-length header and relay segment

## Slide 6
Implementation of Relay Agent Encapsulation for DHCPv4
Experiment result (2)
The relay agents information on the path of DHCP discover
DHCP server could decapsulate RELAYFORWARD message and print all relay agents’ information

## Slide 7
Request comments and fulfillment
Please kindly help to review: draft-ietf-dhc-dhcpv4-relay-encapsulation-01
Last time, there are two reviews suggested. Forget..
Would any people or research entities like to fulfill this draft and make interoperation test with our demo? That will be helpful to find potential errors and push the work forward.

## Slide 8
Thank You