## Slide 1: DHCPv4 Extension for Port-set Allocation
Qiong Sun, Yiu Lee, Peng Wu

## Slide 2: Our request for DHCP extension
We have proposed “lightweight 4over6” in softwire WG.
  draft-cui-softwire-b4-translated-ds-lite
  draft-zhou-softwire-b4-nat
The feedback from the WG
  It is a good and reasonable approach
  We will merge two I-Ds into a single one
So, we need a extended DHCPv4 option for restricted IPv4 address allocation.

## Slide 3: What is Lightweight 4over6 ?
Lightweight 4over6 is an IPv4-over-IPv6 hub and spoke mechanism, which supports address sharing to deal with IPv4 address exhaustion, and places the IPv4 NAT on the initiator side.
A simple extension for DS-Lite without NAT, and address sharing mode for public 4over6.

## Slide 4: Overview
Lw 4over6
initiator
Lw 4over6
Concentrator
Acquire public IPv4 address + Port set
NAT44 within restricted port set
  Tunnel encapsulation/de-capsulation.
Subscriber-level binding record
  Tunnel encapsulation/de-capsulation.
  No NAT anymore
Tunneling
Non-continuous port set algorithms (e.g. GMA in the design team) can be introduced to further improve the security.
[v6 address, v4 address, PSID]
public v4 address,
port set

## Slide 5: Restricted IPv4 address allocation
Initiator would need to get restricted IPv4 address, including
  Public IPv4 address:
    draft-cui-dhc-dhcpv4-over-ipv6: WG item
    the same with public 4over6.
  Non-overlap port-set
    We do not have it yet …

## Slide 6: Considerations on Port-Set Extension
DHCP or PCP
  Since DHCP is more mature and has widely supported, we would prefer to have a extended DHCP option.
DHCPv4 or DHCPv6
  As we need to allocate public IPv4 address to initiator, it would be more reasonable to extend DHCPv4.
Port-set algorithm
  Adopt the port-set algorithm in softwire MAP design team.

## Slide 7: We would like to propose…
A DHCPv4 extension for port-set allocation
It is used for lightweight 4over6 and can be deployed when necessary
Coexistent with draft-cui-dhc-dhcpv4-over-ipv6
We would like to ask DHC WG:
  How do you think of this DHCPv4 extension?

## Slide 8
Thank you 