## Slide 1: Emergency Callback Id
IETF#82, Taipei, Taiwan
draft-holmberg-ecrit-emergency-callback-id-00
(ex draft-holmberg-ecrit-callback-00)
Christer.Holmberg@ericsson.com

## Slide 2: NUTSHELL
Define a new gruu type, emergency gruu (eGRUU), a new SIP-URI parameter (“psapcb”) and a new SIP option-tag (“egruu”) that can help network entities to detect a callback call from a PSAP.

## Slide 3: PSAP CALLBACK REQUIREMENTS
1. Ensure that the PSAP callback call reaches the same device that made the associated emergency call.
2. Identify that the call is a PSAP callback call.
  Applies not only to UA, but also ”home network”, in order to give special treatment (e.g. service disabling) to the PSAP callback call.

## Slide 4: eGRUU CHARACTERISTICS
Constructed as a public GRUU
  “psapcb” SIP-URI parameter included
Must not be constructed locally
Must only be inserted in the Contact header field of a UA (non-PSAP) when making an emergency call
Must only be inserted in the Request-URI of a UA (PSAP) when making a PSAP callback call
Minimal PSAP impact: assume that the PSAP uses the Contact header field URI of the INVITE request for the emergency call when making the associated callback call.

## Slide 5: PROCEDURE: REGISTRATION
UA
REGISTRAR
REGISTER Supported: egruu
200 OK Contact:emg-gruu="sip:callee@example.com;psapcb"

## Slide 6: PROCEDURE: EMERGENCY CALL
UA
PSAP
INVITE Contact:sip:callee@example.com;psapcb
200 OK

## Slide 7: PROCEDURE: PSAP CALLBACK CALL
UA
REGISTAR
INVITE sip:callee@example.com;psapcb
200 OK

## Slide 8: COMMENTS: NEED NEW GRUU TYPE?
Q: Can’t the UA, when making an emergency call, simply insert the “psabcb” parameter in the Contact header field of the INVITE request?
A: A registrar that does not support the “psapcb” parameter might not accept the INVITE request for the PSAP callback call, as the “psapcb” parameter was not provided to the UA in the REGISTER response.

## Slide 9: PROPOSAL TO THE WG
1. AGREE ON PROPOSED MECHANISM
2. MERGE WITH draft-ietf-ecrit-psap-callback

## Slide 10
THANK YOU FOR LISTENING!