## Slide 1: Route Flap Damping Deployment Status Survey draft-shishio-grow-isp-rfd-implement-survey
Shishio Tsuchiya shtsuchi@cisco.com
Seiichi Kawamura kawamucho@mesh.ad.jp
Randy Bush randy@psg.com
Cristel Pelsser cristel@iij.ad.jp

## Slide 2: RFD documentation summary
RIPE-378
RFC2439
draft-ymbk-rfd-usable
Parameter
Consideration /
Recommendation
Architecture
Definition
Route Flap Damping Deployment Status Survey
USE/Not USE
USE/Not USE
Refer/Not Refer
What do you
think?
RIPE-178
RIPE-210
RIPE-229
Parameter
Consideration /
Recommendation Revised
Feedback

## Slide 3: 02
00,01
  the survey was limited in Japan janog@janog.gr.jp
After ietf80,posted the survey to NOGs.
  nanog@nanog.org
  routing-wg@ripe.net
  apops@apops.net
  afnog@afnog.org
  sanog@sanog.org
  lacnog@lacnic.net
Total 63 answered the survey

## Slide 4: Q1.Which is the best description of your job role?
Answer | Number
BGP operator | 27
Researcher | 1
Engineer of vendor | 3
Engineer of Network/System Integrator | 13
Student | 0
Other | 0
Total | 44
This question did not exist for Japan version.

## Slide 5: Q2.Do you use Route Flap Damping ?
Answer | Japan | Global | Total | %
YES | 5 | 8 | 13 | 20.6
NO | 13 | 36 | 49 | 77.8
Skipped this question | 1 | 0 | 1 | 1.6
20.6%(13)
77.8%(49)
1.6%(1)

## Slide 6: Q3.If you select No on Q2,why?
Answer | Japan | Global | Total | %
Do not have the need | 3 | 7 | 10 | 19.6
Did not know about the feature | 2 | 3 | 5 | 9.8
No benefits expected | 3 | 7 | 10 | 19.6
Customers would complain | 1 | 4 | 5 | 9.8
Because I read RIPE-378 | 2 | 13 | 15 | 29.4
Other | 3 | 3 | 6 | 11.8
19.6%(10)
9.8%(5)
19.6%(10)
9.8%(5)
29.4%(15)
11.8%(6)
1 person answered Q3,even if he selected "Yes" on Q2.

## Slide 7: Q4.If you select Yes on Q2,what parameter do you use?
Answer | Japan | Global | Total | %
Default parameters | 3 | 3 | 6 | 40.0
RIPE-178 [RIPE-178] | 0 | 1 | 1 | 6.7
RIPE-210 [RIPE-210] | 0 | 0 | 0 | 0.0
RIPE-229 [RIPE-229] | 0 | 1 | 1 | 6.7
Other | 3 | 4 | 7 | 46.7
40.0%(6)
6.7%(1)
6.7%(1)
46.7%(7)
1 person answered Q4, even if he selected "No" on Q2.

## Slide 8: Q5.Do you know Randy Bush et. al's report ''Route Flap Damping Considered Usable?'
Answer | Japan | Global | Total | %
YES | 12 | 21 | 33 | 52.4
NO | 7 | 22 | 29 | 46.0
Skipped Q5 | 0 | 1 | 1 | 1.6
52.4%(33)
46.0%(29)
1.6%(1)

## Slide 9: Q6.IOS's max-penalty is currently limited to 20K. Do you need this limitation to be relaxed to over 50K?
Answer | Japan | Global | Total | %
YES | 10 | 14 | 24 | 38.1
NO | 9 | 23 | 32 | 50.8
Skipped Q6 | 0 | 7 | 7 | 11.1
38.1%(24)
50.8%(32)
11.1%(7)

## Slide 10: Q7.According to [draft-ymbk-rfd-usable],Suppress Threshold should be set to 6K.Do you think the default value on implementations should be changed to 6K?''
Answer | Japan | Global | Total | %
YES | N/A | 17 | 17 | 38.6
NO | N/A | 18 | 18 | 40.9
Skipped Q7 | N/A | 9 | 9 | 20.5
38.6%(17)
40.9%(18)
20.5%(9)

## Slide 11: Q6.If you have any comments, please fill this box.
Statistical reports from big Service Providers may better visualize the situation.
best current practices is nice, but always needs to be adjusted to reflect local network settings.
We used RFD in the past and came to the conclusion that we do not want to use RFD any more. We still have it configured to be able to get Flap statistics out of our Cisco boxes, but no prefixes get dampended
We recently removed all RFD from the configs due to the information read on the topic among the preso's on the NANOG Archive.

## Slide 12: Q6.If you have any comments, please fill this box. cont’d
after seeing this survey, I read the draft; sounds promising; would be nice to see vendors start to implement it.
Q3, other: Juniper RFD is broken, default values count penalty for both update and withdrawal, and they would not fix that. No clear motivation for us, has caused outage when our customers (with primiary and backup connection to us) had a flapping link.
Strong desire to see the path vector penalized rather than the prefix.

## Slide 13: next step..
Our work almost finished
To provide stable internet,something a damping mechanism is clearly needed.
To consider new technology and new parameter,Current RFD usage survey report is useful for operators and vendors.
So we would like to publish this draft as informational RFC.