## Slide 1: Jumbo Frame Deployment at Internet Exchange Points (IXPs) draft-mlevy-ixp-jumboframes-00.txt
IETF 82
Taipei, Taiwan – 17th November 2011
Martin J. Levy, Director IPv6 Strategy
Hurricane Electric
Presented by:
Cathy Aronson

## Slide 2: draft-mlevy-ixp-jumboframes-00
Abstract
This document provides guidelines on how to deploy Jumbo Frame
support on Internet Exchange Points (IXP). Jumbo Frame support
allows packets larger than 1,500 Bytes to be passed between IXP
customers over the IXPs layer 2 fabric. This document describes
methods to enable Jumbo Frame support and keep in place existing
1,500 Byte communications.
This document strongly recommends that IXP operators choose 9,000
Bytes for their Jumbo Frame implementation.

## Slide 3: draft-mlevy-ixp-jumboframes-00
Internet Exchange Points (IXPs) are vital IP backbones interconnect
  All IXPs are Ethernet layer-2 based these days
  99% of IXPs default to 1,500 Bytes MTU (1,514 Frame)
  A few IXPs that run high MTUs (NETNOD & NASA AIX)
No documentation exists on how IXPs should provide large MTU services
  No standard on large MTU size
  Even the name “Jumbo Frames” is agreed upon
Draft has written with input from various operators
  Been “sitting around for nearly a year” mulling it over
  Sent for review within IXP industry before submitting to IETF

## Slide 4: draft-mlevy-ixp-jumboframes-00
Points covered:
  Force MTU to be consistent over layer-2 fabric
  Propose a consistent MTU value – 9,000 Bytes
  Propose various solutions to implement
    VLAN based (NETNOD & NASA AIX works)
    Duplicate fabric hardware (too expensive!)
  Explain how to do a “flag day” – all change at once!
  Explain how to do BGP – prefer 9,000 Byte path
  Explain pitfalls – misconfigured layer-2 failures

## Slide 5: draft-mlevy-ixp-jumboframes-00
Why 9,000 Bytes?
Too many choices for size based on h/w vendor or h/w version …
  9,000 Bytes
  9,170 Bytes
  9,174 Bytes
  9,180 Bytes
  9,192 Bytes
  9,216 Bytes
The number 9,000 is easy to remember – less confusion
  9,000 Bytes – handle at least 8,192 Bytes user data plus TCP/IP header
See References in draft [JET2007]

## Slide 6: draft-mlevy-ixp-jumboframes-00
Large packets are needed for:
  Mass Data Replication – datacenter X to datacenter Y
  Storage – Amazon S3, MS Azure Storage, iCloud by Apple
  NNTP, DNS zone xfer’s, etc
IXPs are in the path for any-to-any communications
  This draft addresses only ONE element within a data path
Also allows BGP sessions at IXPs to operate with large MSS

## Slide 7: draft-mlevy-ixp-jumboframes-00
Reason to submit to GROW:
  The purpose of the GROW is to consider the operational problems associated with the IPv4 and IPv6 global routing systems, …”
Larger MTU end-to-end traffic can optimize traffic flow and reduce packet overhead
IXPs are a key part of the global routing system
Then – This draft seems to match!

## Slide 8: Q&A
Contact:
  Martin J. Levy
  martin at he dot net