## Slide 1
HIP in 3GPP EPC
IETF 82, HIPRG session, November 17, 2011, Taipei
Zoltán Faigl zfaigl@mik.bme.hu, BME-MIK
Jani Pellikka jpellikk@ee.oulu.fi, CWC
László Bokor bokorl@hit.bme.hu, BME-MIK
Sándor Imre imre@hit.bme.hu, BME-MIK
Andrei Gurtov gurtov@ee.oulu.fi, CWC
Mobile Innovation Centre
Budapest University of Technology
and Economics
Notes: <number>

## Slide 2: Outline
The MEVICO project
HIP roles in EPC and research questions
HIP DEX AKA user access authorization in EPC
HIP signaling delegation services
HIP delegation based inter-GW mobility

## Slide 3: Project description
MEVICO –
Mobile Networks Evolution for Individual Communications Experience
„MEVICO will research the network aspects of the 3GPP LTE-mobile broadband network for its evolution in the mid-term in 2011-2014. The goal is to contribute to the technical drive and leadership of the EPC network (3GPP), and thus support the European industry to maintain and extend its strong technical and market position in the mobile networks market. The results can be used as contributions for further development of the 3GPP standard on EPC in Rel11-Rel13.” [http://www.celtic-initiative.org/]

## Slide 4: Project description
Nokia Siemens Networks Oy
University of Vienna
AALTO University/ School of Science andTechnology (AALTO)
EXFO NetHawk
University of Oulu, Centre for Wireless Communications
VTT Technical Research Centre Of Finland
Alcatel-Lucent Bell Labs France
CEA Centre
France Telecom
Montimage
Artelys
Technische Universität Berlin
Nokia Siemens Networks GmbH
O2 Germany
Deutsche Telecom
Chemnitz University of Technology
Budapest University of Technology, Mobile Innovation Centre
Nokia Siemens Networks Hungary
RAD Data Communications
Ericsson
Ericsson Turkey
Turk Telecom
Avea

## Slide 5: Scalability Problems in Future 3GPP Networks for IP-based Services
Depending on the speed of the data bandwidth increase, constraints for centralized equipments are
  CAPEX/OPEX proportional to traffic volume at busy hour
  Operational constraints to roll out and to upgrade
User traffic anchors in 3GPP: GGSN, PDN GW, HA
Control traffic anchors: P-CSCF, MME
Voice dominant
Data dominant
Revenue
Traffic
Cost of
existing networks
In centralized architecture, an equipment is in charge of allocating an IP address to the terminal and managing the context
  Traffic is anchored in this router
  Tunnels (GTP, MIP, P-MIP) are set up between terminals and centralized routers to transport IP traffic
  Intermediary equipments could also be used to aggregate traffic
Scalability issue concerns the user plane of these centralized equipments when the number of connected users and the bandwidth per user increase
  One context per connected user  mapping between customer profile, IP @, tunnel id, IP-CAN context => required memory and CPU resources
  For each packet, IP routing is made according to user's context and not only on IP header
Notes: <number>
Mobile internet traffic is anchored through GGSN or PDN GW.

## Slide 6: Main objectives
Ensure user plane and control plane scalability for high bitrate data services in 3GPP
  filter out unwanted traffic
  offload traffic to broadband access networks
  increase bachaul and core transport network capacity
  better and adaptive load distribution on transport and service level (distribution of core network functions, multipath communication)
  access technology agnostic
  reduce signaling overhead (attachment, session establishment, handover)
  better QoS support for applications, smart traffic management (application-level traffic identification, E2E QoS for application classes, improved resource selection and caching, multiaccess, access GW selection )
  reduce OPEX of network management (self-organizing network functions)

## Slide 7: Possible roles of HIP in EPC
HIP roles :
  user access authorization.
  IP mobility management for any legacy application.
  network security (e.g, from femtocells to security gateways)
  enforcement of security policies (filters out unwanted traffic)
  load distribution (HIP provides opportunities for smart traffic steering in the HIP peers)
  access technology agnostic, IPv4 and IPv6 coverage
Research questions:
  Support resource-constrained devices / high re-authentication rate
  Support frequent inter-GW mobility without requiring frequent HIP BEXs when HIP is used between the UE and the GW
  Bind HIP transport protocol (e.g IPsec ESP beet mode) with EPC bearers to provide appropriate QoS for different application classes.
  Issues with introducing HIP on 3GPP-access networks

## Slide 8: Introducing HIP on 3GPP-access networks
  3G AKA or 2G SIM based authentication and key agreement already provide user access authorization.
  The benefits of introducing HIP in this case are support for
    multihoming,
    IP-mobility,
    IPv4 and IPv6 interoperability,
    NAT,
    DoS resistance
  The tradeoff between benefits and processing overhead should be considered
  In operator-based environment the cross-layer authorization concept could be used*:
    HIP and IPsec keying material derived from L2 authentication and key agreement procedure
    Binding of L2 and HIP level identity is needed
*[L. Bokor, Z. Faigl, S. Imre, A delegation-based HIP signaling scheme for the ultra flat architecture, in: Proceedings of the 2nd
International Workshop on Security and Communication Networks (IWSCN’10), Karlstad, Sweden, 2010, pp. 9–16.]

## Slide 9: L2 and HIP Level Access Authorization
Problem:
  HIP supports certificate-based peer authorization, or
  The UFA_GWs should maintain ACLs for MN identities, and vice versa
L2 access authorization (assumption):
  EAP(-AKA) (RFC 3748, 5448)
  ERP for fast L2 handoffs (RFC 5296, 5295)
HIP-level:
  Profit from the existing ERP architecture
  We introduce a new HIP access authorization usage type for root keys
New HIP key hierarchy: EMSK/DSRK->hRK->hIK
  hIK mutually authenticates the MN and the local ER server on HIP level
  Cryptographically separated from other root keys, derived keys (used for L2 EAP, ERP)
  UFA_GW proves to be in trust relationship with the local ER server
  Authorization state of the MN and UFA_GW is checked by the aid of the home or local ER server
Independent fast re-authentication on L2 (rIK), and HIP level (hIK).
Key lifetimes
  EMSK ≥ DSRK ≥ DS-hRK = DS-hIK
[L. Bokor, Z. Faigl, S. Imre, A delegation-based HIP signaling scheme for the ultra flat architecture, in: Proceedings of the 2nd
International Workshop on Security and Communication Networks (IWSCN’10), Karlstad, Sweden, 2010, pp. 9–16.]

## Slide 10: L2 and HIP Level Access Authorization

## Slide 11: Distribution of network functions
Main entities involved in distribution
EPC: P-GW, S-GW, MME, PCC functions
IMS: P-CSCF, I-CSCF
Several distribution levels are possible:
Centralized:
  EPC, IMS functions are mainly deployed in the national POP (Point of Presence)
Distributed:
  most of the core functions are deployed in regional POPs
Flat:
  most of the core functions are deployed in local POPs, access sites

## Slide 12: Inter PGW mobility in EPC Release 10
Phase 1 (attachment):
  Authentication/registration to the network
  Authentication/registration to IMS through the P-GW
  UE is allocated with a new IP address
  UE discovers P-CSCF and updates its SIP signaling route in the P-CSCF and the S-CSCF
Phase 2 (session establishment):
  the MN establishes a SIP dialog though P-GW towards P-CSCF.
  establishing a context in the P-CSCF
  informing the P-CSCF about the description of the service (SDP)
  policy rules will be enforced from P-CSCF to the P-GW that will establish a bearer
Phase 3 (inter-PGW handover):
  mobility execution protocol: the UE’ s new IP address will be updated in the network (DSMIP, Proxy MIP)
Notes:
  These phases occur each time the UE mobility induces a P-GW change, in a break before make manner.
  It is very likely that distributed P-GWs offer the same type of a physical access (e.g. through the e-NB). UE should have broken the link with the source eNodeB and source P-GW.
  As phases 1, 2, 3 take time, the handover performance will be impacted.

## Slide 13: Ideas
Simplify user access authorization
  In phase 1 : two user access authorizations (access network and IMS)
  Reduce to one HIP based user access authorization
    What to do if L2 security is also important? See slide on cross-layer authorization
 | authenticator | authentication server
LTE/EPC access | eNodeB (L2 security association endpoint) | MME (+HSS)
Trusted non-3GPP access | access point (L2 SA endpoint) | 3GPP AAA (+HSS)
Untrusted non-3GPP access | ePDG (IPsec endpoint) | 3GPP AAA (+HSS)
IMS access | P-CSCF (IPsec endpoint) | S-CSCF (+HSS)

## Slide 14: EPC Release 10

## Slide 15: EPC Release 10

## Slide 16: Distributed EPC (work in progress)

## Slide 17: HIP-based user authentication in EPC
Jani Pelikka, CWC
Zoltán Faigl, László Bokor, BME-MIK

## Slide 18: HIP-Based Re-Authentication
HIP Diet Exchange with AKA authentication
HIP DEX AKA provides similar functionality as the Internet Key Exchange protocol v2 (IKEv2) with EAP-AKA: it could control user access authentication and authorization of USIM based UEs in non-managed non-3GPP access networks.
Both services provide mutual authentication and establish an IPsec security association pair to protect the path between the UE and the ePDG in the network layer.
HIP DEX AKA is intended as a uniform L3 authentication service on the top of disparate access networks.

## Slide 19: HIP-Based Re-Authentication
Challenges with inter-PDN-GW and inter-ePDG mobility
  Re-authentication in handovers involves multiple protocols (IKEv2 and EAP) of different layers (L3 and L2, respectfully) currently
  The above mentioned protocols induce extensive amount of signaling
  Distributed GWs mean more handovers and re-authentications; heavy frequent cryptographic operations in re-authentications can deplete UE’s battery quickly
Replace 3GPP L2/L3 authentication with HIP Diet Exchange (DEX)
  Utilize the HIP protocol combined with 3GPP AKA method, as well as the corresponding keys in handovers; similar to Fast Initial Authentication (FIA)
  Utilize a lightweight L3 HIP authentication scheme, HIP Diet Exchange
  Removal of L2 authentication protocols (i.e. loose the EAP protocol)
  Reduction of elements in the authentication (i.e. an AAA/EAP server)
Anticipated benefits of the proposal include the following:
  Faster handovers, as re-authentication process is improved due to disinvolvement of L2 protocols and elements other than HIP and a backend authenticator (e.g. HSS) and GW, respectively
  Lower computing and signaling overhead on and between GW and UE
Notes: <number>

## Slide 20: HIP-Based Re-Authentication

## Slide 21: HIP-Based Re-Authentication
Real-life implementation and testbed validation
Validation status
  HIP-DEX base protocol implemented in the C++ language for GNU/Linux
  Two versions of HIP-AKA implemented in the C++ language for GNU/Linux
    One is running in a testbed at CWC premises
    And the other in a testbed at BME-MIK premises
Validations will use both BME-MIK’s testbed and CWC’s testbed
  In the beginning, validations are carried out using only the BME-MIK’s more extensive testbed (Wi-Fi and UTRAN accesses supported); though some measurements and development work is done using the CWC’s testbed
  Testbed configurations emulate the flat (long-term) MEVICO LTE architecture
  Later, bootstrapping and Femtocell (possibly DEX used on L2) studies will be performed in CWC’s testbed
  We also intend to run our protocol in resource constraint mobile devices such as Android smart phones
Notes: <number>

## Slide 22: Validation environment (BME-MIK)

## Slide 23: Preliminary results for CPU and memory measurements
Method | CPU load (UE) [clock cycles * 106]
HIP BEX (infraHIP) | 64.2
HIP DEX AKA (CWC) | 13.0
HIP DEX (CWC) | 6.4
IKEv2 EAP-SIM (ikev2 project) | 28.5

## Slide 24: Results for IKEv2 (for comparison)
[Z. Faigl, S. Lindskog, and A. Brunstrom, "Performance evaluation of IKEv2 authentication methods in next generation
wireless networks" Security and Communication Networks, 3: 83–98, 2010, doi: 10.1002/sec.114]

## Slide 25: HIP signaling delegation services providing inter-GW mobility
Zoltán Faigl, László Bokor, BME-MIK

## Slide 26: Delegation-based HIP mobility service in distributed/flat architectures
Problem statement
  Inter-GW mobility requires new mechanisms to avoid unnecessary HIP BEX
  Reduce signaling overhead on the air interface
General solution
  Introduce signaling delegation service for HIP
    Enables HIP host association and IPsec SA establishment by a delegate. Secure security context transfer is needed from delegate to delegator (CXTP over IPsec)
    Enables HIP BEX, HIP updates by a delegate
  Delegation introduces a new hop-by-hop traffic forwarding scheme providing flow mapping in the GWs based on fivetuples
    This reduces significantly the number of E2E HIP host associations and IPsec SAs in the network,
    Better for traffic management, legal interception
Using these services, inter-GW mobility can be performed without complete reassociation (HIP BEX)

## Slide 27: Traffic forwarding

## Slide 28: Motivations for „hop-by-hop” traffic forwarding
E2E HIP concept does not fit 3GPP because several functions in the GW require information above the network layer.
  Application classification, user clustering
  Application class based QoS enforcement
  Deep packet inspection for network monitoring and network management
  Legal interception
  etc.
E2E concept requires much more HIP BEXs and updates in the network.
This separation enables the introduction independent addressing and routing mechanisms in the access networks and the core network

## Slide 29: Performance evaluation of Hop-by-hop vs. E2E HIP
Zoltán Faigl, BME-MIK

## Slide 30: Macroscopic analysis
Transport
Objective: average number of HIP BEXs per unit time due to attacment and session establishment
GW
GW
MN
MN
MN
MN
GW
M – number of GWs
α – attachment rate (Poisson)
ω – detachment rate per MN
λ – session establishment rate per MN
µ - session ending rate per MN
T – unused association lifetime
γ – average mobility rate per MN

## Slide 31: Average number of HIP BEXs per unit time
Attachment – detachment is modeled with a birth-death process
  Poisson arrival α, exponential service times n*ω, n=0..∞ is the state number, i.e., number of attached users
  Expected number of attached users is α/ω
Session establishment and ending rate
  Birth-death process
  E2E case : states represent the number of existing application sessions between a given pair of MN
  UFA case : states represent sessions between a given pair of GW
  Death rate: k* µ, session ending rate, k is number of sessions between the two entities
  Birth rate: arrival rate of sessions,
    Requires assumptions on the
      topology (in UFA case),
      call desination distributions (both cases)
    Simple assumptions for macroscopic view:
      users are uniformly distributed among GWs, and
      destination selection has uniform distribution
λi = λ
µi = iµ
Birth-death process:

## Slide 32: Average number of HIP BEXs per unit time
unused HIP association is closed after a constant time (T)
number of HIP BEXs per unit time between a pair =
  probability of zero sessions (state 0) between a pair ∙
  probability that sojourn time in state 0 is greater than T ∙
  transition rate from state 0 to 1
cumulated number of HIP BEXs per unit time
  E2E: (%∙number of MN pairs
  UFA: (%∙number of GW pairs) + α
Ratio of the average number of HIP BEXs per unit time is given in the next slides (UFA compared to E2E)

## Slide 33
# of attached users : 1.3M
avg. # of sessions:
bw MNs: 4.63e-06
bw GWs (1000 GW): 7.78

## Slide 34
# of attached users : 222
avg. # of sessions:
bw. MNs: 4.52e-02
bw- GWs (10 GW): 22.2
unused association lifetime:
(1) 15min, (2) 1 min

## Slide 35: HIP delegation services
Zoltán Faigl, László Bokor, BME-MIK
[L. Bokor, Z. Faigl, S. Imre, A delegation-based HIP signaling scheme for the ultra flat architecture, in: Proceedings of the 2nd
International Workshop on Security and Communication Networks (IWSCN’10), Karlstad, Sweden, 2010, pp. 9–16.]

## Slide 36: Registration to HIP delegation services
The Delegate gets an Authorization Certificate (or Token) from the Delegator that will assure the CN that the Delegate can proceed in Delegator’s name

## Slide 37: Type 1 Delegation Service and CXTP
Type 1 Delegation Service requires
  pre-existing IPsec SA between the Delegator and the Delegate, and
  HIP host association between the Delegate and the CN.
Delegate
  establishes new HIP and IPsec SA with the CN, in the name of the Delegator. Instead of HIP BEX, simple key derivation is used.
  sends to the Delegate the new HIP and IPsec SA contexts using CXTP protocol protected with IPsec

## Slide 38: Details

## Slide 39: Type 2 Delegation Service
The Delegate
  executes HIP Base Exchanges (BEX), HIP Updates, IPsec SA establishment in the Delegator’s name, with the Delegator’s authorization
  maintains the established HIP and IPsec associations for Delegator (periodic rekeyings)
  ~ and the Delegator notify each other in order to create the HIP host association states also in the Delegator. These HIP host associations use the existing IPsec SA bw. the Delegator and the Delegate as transport protocol.

## Slide 40: Details
Notes: <number>

## Slide 41: Inter-GW mobility using 802.21 and HIP delegation services
Proactive handover procedure
  802.21 initiation phase: the GW configures QoS thresholds on the MN
  802.21 handover preparation phase, decide target GW: the GW queries resource information from candidate PoAs, paramters from the MIH Information service, and decides on the target GW
  HIP handover preparation: HIP and IPsec contexts are established for the MN - target GW, target GW - peers of the MN , traffic is routed through [MN, current GW, target GW, peers]
  802.21 commit phase: establish L2 resources on target PoA and triggers physical handover
  Physical handover, L2 reattachment
  802.21 release resources: release resources, update traffic path: [MN, target GW, peers]
[Z. Faigl, L. Bokor, P. Miguel Neves, K. Daoud, P. Herbelin, @Evaluation of two integrated signalling schemes for the Ultra
Flat Architecture using SIP, IEEE 802.21, and HIP/PMIP protocols", Elsevier, Computer Networks 55 (2011) 1560–1575]

## Slide 42: HIP handover preparation
Prerequisites:
  the target GW registers to the Type 1 Delegation service of the source GW,
  the source GW subscribes to the Type 2 Delegation service of the target UFA GW, HIP
Handover preparation:
  location update of the MN by the target GW
  the target GW delegates HIP and IPsec association establishment to the source GW

## Slide 43: Handover preparation procedure on HIP layer

## Slide 44: Handover preparation procedure on HIP layer

## Slide 45: 802.21 Commit phase

## Slide 46: Handover completion phase

## Slide 47: HIP Delegation based mobility services
Simulation based validation (OMNeT++, HIPSim++)
Validation status
  Only terminal mobility
  Delegation-based HIP implemented, 802.21 handover preparation is hardcoded, i.e., proactive handover is triggered „manually”
  Micro-HIP and HIP mobility services are implemented for comparison (i.e. for reference results)
Test scenarios
  Both terminal and network mobility will be considered
  UE is moving in the network between different access networks. Intra- and inter-PGW mobility events
  Measurements to be done in different distribution levels of GWs, i.e. flat, distributed, centralized topologies
  Mobile IPv6 and NEMO BS will also be used for reference
Notes: <number>

## Slide 48: HIP Delegation based mobility services
Validation metrics, or KPIs include the following:
  Handover delay on HIP layer
  UDP packet loss
  TCP throughput
  Voice quality degradation (Perceptual Evaluation of Speech Quality - PESQ) using VoipTool
Future work within the MEVICO project (2H11, Y12)
  Provide different distribution-level reference scenarios for the simulation (2H11)
  Implementation and evaluation of the delegation-based HIP-NEMO designed for flat architectures (1H12)
  Introduce MIPv6 and NEMO BS reference models and measurements (1H12)
  Run measurements (1H12)
  Enhance the applied 802.21 model in INET/OMNeT++ (2H12)
  Publish results (2H11, 2H12)
Notes: <number>

## Slide 49: HIP-UFA Mobility simulation results
László Bokor, BME-MIK

## Slide 50: Simulation results: Topology
Modeling and implementation of the integrated HIP + IEEE 802.21 MIH mechanisms and evaluation against standard HIP macro-mobility and micro-mobility solutions
  INET/OMNeT++ based HIP simulation framework (HIPSim++*)
  INET’s Notification Board based IEEE 802.21 MIH simulation model
  Results show the power of the integrated scheme
* [L. Bokor, Sz. Nováczki, L. T. Zeke, G. Jeney: „Design and Evaluation of Host Identity Protocol (HIP) Simulation Framework for INET/OMNeT++”, in the proceedings of the 12-th ACM International Conference on Modeling, Analysis and Simulation of Wireless and Mobile Systems (MSWIM 2009), ISBN:978-1-60558-616-8, DOI: 10.1145/1641804.1641827, pp. 124-133, Tenerife, Canary Islands, Spain, 26-30 October 2009.]

## Slide 51: Simulation results: HO Latency
The latency was defined here as the time elapsed between loosing the connection at the old AP and the mobile sending out the last mobility management related signalling packet (e.g., HIP UPDATE packet) while connected to the new AP
  The integrated scheme is independent of the RA interval!

## Slide 52: Simulation results: UDP Packet Loss
How many UDP packets are lost during a handover in a HIP system in case of different UDP traffic?
  UDP results are in line with the measured handover latencies and show the power of the proactive HIP+802.21 solution!

## Slide 53: Simulation results: TCP Throughput
TCP Reno traffic was originated between the HIP initiator and responder (i.e. the wired and wireless HIP nodes)
We measured the throughput of one minute experienced at different handover frequencies
  Every point represents the average throughput of 100 measurements applying the same value for the number of handovers per every minute of that series
  Between the runs we increased the number of handovers suffered per minute form 0 to 9

## Slide 54
Thank you for your attention!
Any questions?