## Slide 1: The HIP Diet Exchange HIP DEX
Robert Moskowitz
Verizon
Innovation Group
November 17, 2011
rgm@labs.htt-consult.com

## Slide 2: Purpose of this presentation
Why HIP DEX
An update on HIP DEX progress
  Status of Draft
  Next steps

## Slide 3: Why HIP DEX
VERY Constrained Devices 'resist' Key Management
  At best rely on static secret as Asymmetric Cryptography too expensive
ECDH His
  'Only' need wide multiply
  Static ECDH
    Only Crypto function added to devices
      Have AES-CCM in Layer 2
  No signing
    No Crypto Hash
  MACing only
    CMAC
    KEYmat via CMAC as well

## Slide 4: Implication of loss of SIGNing
Replacing SIGNing with MACing results in
  Loss of non-repudiation
Major impact to UPDATE packets
  Note that UPDATE packets are now used to distribute pair-wise and group keys

## Slide 5: Status of HIP DEX?
Draft update in progress – 06.txt
Still need to reconcile common text with 5201-bis
Change from AES-CBC to CTR for Encrypted_Key
Need review of KDF function based on CMAC
  E.G. Additional info part of extract phase which is not included in draft SP800-56C
Need to solidify HIT derivation
Need review of Key wrapping of session keys

## Slide 6: Next Steps
IEEE 802.15
  New PAR, 802.15.9, will provide 'shim' for transport of KMP datagrams
    This is KMP agnostic
  Mandates using 802.15.4e Information Elements
  Use cases and guidelines for using HIP (both BEX and DEX) for 802.15 KMP
  Work starting in Jan '12

## Slide 7: Next Steps
6lowpan
  Draft for Dispatch ID for 802.15.9 KMP shim
    For pre-4e devices
    'Port access' control may be a little complex on 4e compliant controller
      Both 4e and pre-4e sensors in PAN

## Slide 8: Next Steps
CORE
  Basically a subset of HTTP
  CORE has selected DTLS for their security protocol over ESP, as the app has direct knowledge of the presence or lack of security
  If certificates are supported in the sensor, then EAP-TTLS will be used for the KMP
  If no certificates then DTLS-PSK will be used
    No specification of source of PSK
  Adding TLS-Rawkey
    Sound familiar?

## Slide 9: Next Steps
CORE
  Minimally develop ID for using HIP DEX as source of PSK for DTLS-PSK
  And/or develop ID for HIP DEX for use with DTLS datagrams
    Maybe not too hard to do for sensor
    But may be really hard to do for server

## Slide 10
Questions?