## Slide 1: Hierarchical Prefix Delegation in Basic Home Networks
draft-chakrabarti-homenet-prefix-alloc-01.txt
Erik Nordmark
Samita Chakrabarti
Suresh Krishnan
Wassim Haddad

## Slide 2: Goals
Look at existing IPv4 home networks with multiple NATs
How can we add IPv6 to those without any IPv6 NATs?
H
ER
CER
CER
IR
IR
IR
IR
H
H
H
H
H
H
CER
IR
IR
IR
H
H
H
H
H
H
H
IR
IR
IR
H
A. Tree of routers
B. Daisy chain of Routers
C. Internal host multi-homing

## Slide 3: Why multiple Customer Routers today?
ISP provides a box, perhaps with a single Ethernet port and no WiFi
  That box does NAT
  Customer wants multiple Ethernet ports, WiFi
Dedicated VoIP box is also a NAT; should be closest to the ISP for QoS reasons
Backup box can also be a NAT
Result is a daisy-chain or shallow tree of NATs

## Slide 4: State of current IPv4 home routers
Have a dedicated uplink port with DHCP client
Have zero or more downlink ports
  Might be bridged together
  WiFi might be bridged together with Ethernet
Might support a separate guest network
  Unclear whether this is a separate IPv4 subnet or just ACLs
Model as one or more downlink L3 interface
  With optional bridges below those interfaces

## Slide 5: Core of proposal
Just use DHCPv6 Prefix Delegation
  Run a PD client on the uplink interface
  Run a PD server for the set of downlink interfaces
Start PD server once a prefix is available from the uplink/client
  ULA discussion on subsequent slide
Carve up the delegated /N prefix to provide
  Some /64 prefixes to assign to the routers downlink interfaces
  Some /(N+k) prefixes to sub-delegate to downlink routers

## Slide 6: Recommend default k=3
Allows for 7 downlink routers
Allows for 3 levels of hierarchy from a /56
  Customer edge router sub-delegates 7 different /59 prefixes
  A interior router one step down can sub-delegate 7 /62 prefixes
  Two steps down a router can have four interfaces, or sub-delegate two /64 plus have two interfaces
In general and approximately,
  k = log2(expected number of downlink routers + 1)

## Slide 7: Prefix Stability
Each router calculates its fixed sub-delegation prefix length
Recommend that routers (their PD server) remember delegated prefixes in stable storage
  Even after the lease has expired
  Do FIFO allocation so that a previously used prefix will be re-used last
Or recommend that requesting router (PD client) remember the prefix it had before

## Slide 8: ULA
Manually configure the CER to generate a ULA prefix for the home
Sub-delegate ULA by itself (if home has never been connected)
Sub-delegate ULA together with global prefix
Possible with further automation
  If PD client receives global prefix but no ULA from delegating router, then assume it is the Customer Edge Router; enable ULA generation and sub-delegation
  Is this automation desirable? Security concerns?

## Slide 9: Site Multi-homing
With IPv4 NAT two separate home routers connecting to different ISPs (and wiring together their downlink ports) doesn’t work well – dueling DHCP servers on the same link
A single IPv4 NAT connected to two ISPs work – Ditto for this proposal
H
CER
IR
IR
IR
H
H
H
H
H
Prefix from ISP-A
Prefix from ISP-B
CER delegated both prefixes
and
CER is able to route/forward
Upstream Packets to respective ISPs
Based on the source prefix

## Slide 10: Next Steps?
Note that this approach addresses a near term need of enabling IPv6 in home routers without NAT
  Complementary to the larger desire to have arbitrary topology home networks, redundant paths, etc
Should the WG work on this?
Make it a WG document?