## Slide 1: Advanced IPv6 Residential Security draft-vyncke-advanced-ipv6-security-03
Eric Vyncke ev@cisco.com
Mark Townsley townsley@cisco.com
Andrew Yourtchenko ay@cisco.com
November 2011

## Slide 2: Advanced Security
User Feedback
User control
IPS
Dynamic Policy & Signatures Update
On-line Access to IP Address Reputation
In short: traffic is allowed until proven guilty
CPE or internal router

## Slide 3: Overview
7 policies are identified in the -03. These are largely based on features which are commonly available in “advanced” security gears (UTM) for enterprises for several years
Home edge/internal router is not something that is purchased and thrown away when obsolete. Instead, it is actively updated like many other consumer devices are today (PCs, iPods and iPhones, etc.)
Business model may include a paid subscription service from the manufacturer, a participating service or content provider, consortium, etc.

## Slide 4: Why is this important to IPv6 & HOMENET?
RFC 6092 defaults to inbound-disallowed (transparent mode is an option) and will break end-to-end in HOMENET configurations
‘intra-home’ router does not always have trusted vs. untrusted sides
Security policy can be adjusted to match the threat as attacks arrive
We don’t break end-to-end IPv6, unless we absolutely have to

## Slide 5: Opening THE Can of Worms NAT is Useless for Security
Most botnet members are behind a NAT
  Malware are downloaded nowadays…
Allowing PCP or UPnP to open NAT pin-holes puts a huge trust in the host integrity
There is a need to apply security between guest and home security domains

## Slide 6: Default Security Policy
RejectBogon:
  including uRPF checks
BlockBadReputation:
  for in/outbound traffic
AllowReturn:
  and apply IPS on in/outbound traffic
AllowToPublicDnsHost
  Allow inbound traffic to inside host with a AAAA & reverse-DNS
ProtectLocalOnly:
  Block all inbound traffic to inside which never transmitted to the outside (à la full-cone)
CrypoIntercept:
  Intercept all inbound SSL/TLS connection, present (self-signed) cert, decrypt and re-encrypt
  Goal is to apply IPS
ParanoidOpeness:
  Allow ALL inbound traffic by default
  See more next slide

## Slide 7: More on Paranoid Openness
Rate limit (SYN & plain data)
  To protect low-bandwidth residential links
  Basic protection against host scan
If authenticated flow (e.g. HTTP)
  Perform dictionary attack on credential and reject too obvious ones (or default ones)
  Goal is to force user to select good credentials
IPS must be applied
  If protocol unknown, then flow MAY be permitted
  If attack is detected, then flow MUST be denied

## Slide 8: -00 at IETF 76
-00 presented at V6OPS & SAAG
Globally positive reaction
  The crypto part could be improved/better presented
  Paranoid Openness is very much needed for IPv6
  Already known as Universal Threat Mitigation for large enterprises
  Could/should cross pollination with simple-security ID

## Slide 9: Between IETF76 & 82
But, little progress done (Eric’s & Mark’s fault)
-03 delta
  Some cosmetics
  More reference to UTM
  Reference to previous I-D & RFC 6092
  More consistent with HOMENET