## Slide 1: Prefix allocation in small networks
Fred Baker

## Slide 2: Allocating prefixes
Methods:
  Manually (let’s not)
  Automatically using DHCP/DHCPv6
  Automatically using Netconf
  ZOSPF suggests allocating a more-or-less random number
  Automatically using something else TBD
Central vs Distributed
  Netconf implies central configuration control
  DHCP supplies parameters to what is otherwise a distributed control
Questions we have to ask ourselves:
  Do we want to presume central or distributed configuration control?
  Do we want/need to build a protocol here?

## Slide 3: ZOSPF solution
Algorithm:
  The CPE advertises an IA_PD into the domain using some (new) LSA
  Each router selects a random number that no other router (type 9 prefix) is using
Race condition:
  What if two or more routers are coming up simultaneously, such as after a power outage?
    Some probability that they select the same number.
    There is some logic to manage this; needs testing.

## Slide 4: I suggest we assume distributed control and DHCP/DHCPv6:
Protocol is defined, and provably works
It can be specified as an operational procedure
We don’t need a new protocol
We don’t want to write a yang module

## Slide 5: Typical configurations: the watchword is “simple”
ISP
ISP
ISP
ISP
ISP
Single router with
some number of
subnets
Multi-router
Tree network
Multi-router
generalized
network
Multihomed
network

## Slide 6: Simplest case: only one router
If there is only the CPE Router, it
  Is allocated a prefix by the upstream network
  Assigns /64s from that to each interior network
No added complexity
ISP

## Slide 7: Next-simplest case: Tree Network
CPE Router
  Is allocated a prefix by the upstream network
  Assigns /64s from that to its interior networks
Interior routers
  Request allocation from DHCP Server in CPE Router for their LANs
ISP

## Slide 8: Multihoming
Distributing prefixes from more than one subnet
Calls for parallel distribution
ISP
ISP

## Slide 9: Where distributed allocation gets hairy
If the network has redundant topology
  There is some probability of multiple routers on a downstream LAN creating different subnets on the same LAN simultaneously
Architecturally not an issue
Practically, suboptimal
Solution:
  Minimize the probability of occurance
ISP

## Slide 10: Minimizing probability of simultaneous allocation
At least two approaches:
  Somehow select one router on the “subsequent” LAN to ask for a prefix
    Example: OSPF/IS-IS DR asks for the prefix
  Allocate prefixes from the server at a slow enough rate that duplicate allocation is improbable
  …?