## Slide 1: Prefix Assignment and distribution of other configuration infromation
Ole Trøan @Homenet IETF82

## Slide 2: Problem:
How to assign stable prefixes to links in an arbitrary topology home network?
How to distribute other configuration information (DNS servers etc)?
  Given multiple sources of information

## Slide 4: Possible Solutions (interim):
Layer 2/RFC6204 topology – null solution
Multilink subnet routing
    Hosts routes combined with ND flooding (draft-ietf-ipv6-multilink-subnets-00)
Hierarchical DHCP Prefix DelegationRFC3633 + draft-chakrabarti-homenet-prefix-alloc-00
Flat DHCP Prefix Delegation
  RFC3633 + draft-baker-homenet-prefix-assignment-00
Zeroconf OSPF
  draft-arkko-homenet-prefix-assignment-01
NAT (IPv6 NAT or NPT66)
Others

## Slide 5: Consider: Flooding vs Request/Reply
Request/Reply may require a God server
  Make handling multiple sources of information difficult
Request/Reply requires some way of discovery of the “server”.
Flooding is distributed state. All routers in the network has the same view of the network. Assuming link-state routing here.
  Requires “collision detection”
Both assumes fate sharing that the node injecting site-prefix or being the server are co-located with the border router