## Slide 1: The Holy Grail of Smart Object Interoperability
The Process Automation Arena
  Robert Assimiti

## Slide 2: Many Hands - Even More Gloves
Million $ question: How do we pave the way towards interoperable and secure connectivity among smart objects in an application and link-layer agnostic manner?
Current reality: A wide gamut of standards bodies have tailored application (even niche) and link-layer dependant solutions.

## Slide 3: Use Case: Smart Objects in the Process Automation Arena
OnWorld conducted polls and published results based on interviews with 105 plant managers, process integrators and system engineers
Results are clearly indicative of industrial end user’s concerns
IPv6 addressability and standards compliance are major factors for adoption of smart objects employed in process and factory automation
IPv6 compliance is tightly coupled with future extensibility of smart objects based products
Source: “Industrial Wireless Sensor Networks,” ON World March 2010
Notes: OnWorld published a comprehensive report in the spring of this year targeted at adoption of wireless in industrial applications.
The results are based on interviews with 105 plant managers, process integrators and system engineers.
The figure to the right is presented as courtesy of the OnWorld group.
It collects and lists the main end user’s concerns as related to adoption of wireless in industrial applications.

## Slide 4: Industrial Smart Object Networks
Fully deterministic and centralized networks
Scalability in the hundreds
Extremely high reliability -> dire consequences associated with failure: 99.9999999% (even in wireless nets)
Path diversity a must
Must meet strict guaranteed latencies: sub-second even in multi-hop wireless networks
Relies heavily on push model for periodic data collection: as frequent as every 100 ms)
Support for P2P control loops
Long battery life: 5 -10 years

## Slide 5: The Current Global Trifecta
Standard | ISA100.11a | Wireless HART | WIA-PA
Networking | IPv6/6loWPAN | Standard specific | Standard specific
Transport | UDP | Standard specific | Standard specific
Routing | Mesh-under but RPL not precluded | Mesh-under | Mesh-under
Web services | None | None | None
Management | Standard specific | Standard specific | Standard specific
Security (end-to-end) | Standard specific at transport layer | Standard specific at application sub-layer | Standard specific at application sub-layer
Provisioning | Standard specific | Standard specific | Standard specific
Backbone networking | IPv6 | Standard specific | Standard specific
Standard specific means lack of alignment with IETF existing and vetted standards.
Standard specific dominates the map at this point. That is so 20th century!!!

## Slide 6: Smart Objects– The Chimera Threat
Wide gamut of application requirements resulted in deployed networks that exhibit:
Various degrees of scalability
Messaging patterns:
  Bidirectional Client server
  Push
  Alerting
Distributed versus centralized network management paradigms
“Sleepy” versus “always-on” devices
Various latency guarantees
Different security paradigms and policies
High variability in hardware resources (memory, processing power, etc)
Chimera: “A fire-breathing monster with a lion's head, a goat's body, and a serpent's tail.”
THREAT: The smart object ecosystem will end up as a chimera of networking technologies.

## Slide 7: The Holy Grail of SO Interoperability
Holy Grail:
  No middleboxes/translation gateway
  Networking and security should be interoperable and independent of application and link layer
A good starting point:
  Standardize capability discovery to allow smart objects to learn whether they can interoperate
  “You might say that I’m a dreamer, but I’m not the only one.”