## Slide 1: Smart Objects and the Internet Architecture
Fred Baker

## Slide 2: RFC 6272
I wrote, with a lot of help, a document describing the RFCs we write and use as a toolbox from which one can build products
  This was requested by US NIST for the purposes of the Smart Grid
If I don’t say so myself, it’s recommended reading

## Slide 3: ...the Network should enable an application in a particular domain to communicate with an application in any other domain in the information network, with proper management control over who and where applications can be interconnected.”
NIST Roadmap, Version 1.0, September 2009

## Slide 4: We have some real challenges out there
Picking one…
  Car companies tell us they want to burn a 128 bit address into an automotive appliance and use it to talk with the car’s “mother ship”
    Services similar to OnStar
    Automotive maintenance reports
  No comprehension that the IP Address presumes an Internet Architecture in which the prefix is a locator, and has to be scalably routable by the ISP
  No comprehension that an IP datagram is routed from and to a customer…
A better alternative: an architecture for trusted communications
  Whatever address I am using, I identify myself to my peer using protocol exchanges such as HIP/ESP or D/TLS

## Slide 5: Don’t misunderstand the intent of networks of Smart Objects
They don’t all intend to use the Internet as we understand it
  Smart Grid, specifically, likely to be a parallel network for the most part
They do plan to use IP and some of the related protocols
  If a protocol doesn’t meet their needs, they plan to change or replace it
  Health care likely a VPN, IPsec Transport Mode, https, or D/TLS-based

## Slide 6: DOE / NIST / UCAIug / ASAP-SG Security Effort
US DOE FFRDC’s

## Slide 7: What kinds of security mechanisms?
Communication Layer | Type of control | Example
Data Content | End to end integrity in message-based exchange | W3C XML Signature
Application Layer | Application to application authentication, authorization, encryption | TLS, HTTPS, DKIM, S/MIME, SSH
Network Layer | System-to-system authentication, authorization, encryption | IPsec ESP
Physical/Link Layer | Limited Membership | SSID, IEEE 802.1X with EAP-TLS