## Slide 1: Garrulity and Fluff
Carsten Bormann

## Slide 2: a decade of sensor network research
everything has to be done in a different way
  Internet protocols use too much:
    energy
    spectrum
    gates ...
greenfield architectures, future internet, etc.

## Slide 3: the problems are real
constrained nodes
  little power (~ µW), lots of sleeping
  little ROM (code space), RAM (state)
constrained networks
  high loss
  not an Ethernet (multicast, reliability, ...)

## Slide 4: wait, we heard this before
Attempts at redoing everything for some 10x quantitative reason:
  “lightweight protocols” (XTP and friends)
  WAP
  ATM
  ...

## Slide 5: why did WAP&co fail?
(insert reason here) +
Moore’s law
  In the time you need to get 10x performance out of a new architecture, Moore’s law gives you 10x performance with the old architecture

## Slide 6: in constrained node/networks, Moore’s law barely applies
In the low-power, low-cost area, gains from Moore’s law are used
  to save power
  to save cost
Performance, ROM, RAM grow very slowly

## Slide 7: meanwhile...
people are building the Internet of Things
focus on what we can do while maintaining much of the Internet architecture
“Embedded Internet”

## Slide 8: what hurts
architectural issues
garrulity
fluff

## Slide 9: please re-calibrate your complexity meters
code is expensive
  “class 1” = 100 KiB, “class 2” = 250 KiB
state is expensive
  “class 1” = 10 KiB, “class 2” = 50 KiB
packets are expensive
listening is even more expensive
  and multicast doesn’t work

## Slide 10: current approaches
some protocols can be fixed
  ND ➼ 6LoWPAN-ND
some protocols can be re-used after removing sources of complexity
  e.g., DTLS without X.509
some architectures can be re-used with more appropriate protocols
  e.g., reincarnate HTTP’s REST in CoAP
= retargeted for less generality, more austerity

## Slide 11: your protocol may be next
unless it only runs on aircraft carriers and up
If not, start thinking about ways to:
  reduce garrulity
  actively get rid of fluff
http://www.iab.org/wp-content/IAB-uploads/2011/04/Bormann.pdf