## Slide 1: VPLS Multi-homing
draft-ietf-l2vpn-vpls-multihoming-03
Kothari, Kompella, Hendrickx, Balus, Uttaro

## Slide 2: Draft has been stable
… so, time to shake things up :-)
BGP DF election (more accurately, BGP route selection) as defined today has two problems:
  Route oscillation
  Longer than needed convergence and unnecessary traffic blackholing

## Slide 3: Route Oscillation
RR1 receives RT1 from PE and RT2’ from RR2. RT1 and RT2’ are the same route (from PE). How should RR1 choose between them?
RR2 has the same problem
If RR1 chooses RT2’ and RR2 chooses RT2, life gets difficult
RR1
RR2
PE
CE
RT1
RT2’
RT2
RT1’
The VPLS route for CE is advertised by PE to RR1 and RR2 as RT1 and RT2, respectively; RT1’ and RT2’ are these same routes re-advertised by RR1 to/from RR2

## Slide 4: Route Oscillation (2)
RR1 gets RT1 from PE. RR2 gets RT2 from PE
RR1 chooses RT1 as best path (only path)
  RR2 chooses RT2 as best path
RR1 advertises RT1’ to RR2
  RR2 advertises RT2’ to RR1
RR1 redoes route selection, picks RT2’ instead of RT1 this time. RR2 similarly picks RT1’

## Slide 5: Route Oscillation (3)
RR1 has a new best path, that of route RT2’; so it tries to re-advertise RT2’ to RR2. But the best path is from RR2! Loop. So RR1 withdraws RT1’
  Similarly, RR2 withdraws RT2’
With RT1’ and RT2’ withdrawn, we’re back to step 1. Oscillate.

## Slide 6: Long Convergence + Blackhole
The current DF election rules say nothing about choosing between VPLS routes learned via eBGP and iBGP
  Choosing an iBGP route means you are subject to the iBGP rules of not re-advertising that route to iBGP peers
  Not getting that route may mean no backup path
  This can adversely impact convergence time and cause a short blackholing of traffic

## Slide 7: eBGP vs. iBGP
AS1
AS2
RR1
RR2
RR3
eBGP
iBGP
?
If RR1 prefers RR2’s route (iBGP) over RR3’s route (eBGP), it will not advertise to its client PE1
PE1
PE2
Colored lines with arrows indicate VPLS route advertisement/re-advertisement

## Slide 8: Solution
Being wrangled, arm-wrestled and worked on in real time
IDR chair suggests using standard BGP route selection in place of BGP DF election
  This would simplify things protocol-wise, and bring back preference of eBGP over iBGP
  However, there are issues with backward compatibility that need to be worked out

## Slide 9: {VPLS|BGP} DF Election
A philosophical issue stems from focusing on “DF election” versus “route selection”
  DF election focuses on choosing among multi-homed sites to be the Designated Forwarder
  However, there are times when one sees the same (single-homed) route from different peers with different paths and must choose among them
A slight rewrite of the algorithms to reflect this would be helpful

## Slide 10: Route Distinguishers
RFC 4761 says that PEs supporting multi-homed sites MUST use (be configured with) the same Route Distinguisher (RD)
  However, it is now common practice to use different RDs for multi-homed sites in IP VPNs
  This practice gives BGP “add path” for free
One more thing to think about: should this draft suggest (or require) this newer practice?