## Slide 1: SPB over MPLS draft-mack-crane-l2vpn-spb-o-mpls-00.txt
82nd IETF Taipei
<number>
Ben Mack-Crane ben.mackcrane@huawei.com
Lucy Yong lucy.yong@huawei.com
Notes: <number>

## Slide 2: About This Draft
82nd IETF Taipei
<number>
Describe use cases for SPT sites interconnected by an IP/MPLS network to form one STP Region
  Point-to-Point PW
  PW mesh
Introduce a new Hierarchical L2VPN architecture with SPT Bridge and IP/MPLS
Informational draft

## Slide 3: Shortest Path Bridging (SPB)
IEEE standard: 802.1aq
  Optimal pair-wise data frame forwarding with arbitrary topology
  Deterministic behavior
  Compatible with existing VLAN hardware implementations
SPB enabled device is called an SPT Bridge
  Because it computes Shortest Path Trees (SPTs)
SPBV (SPB – VID mode) provides SPB with no configuration for customer LANs (e.g., home or small office)
SPBM (SPB – MAC mode) provides a SPB backbone LAN for connected customer bridges or end stations (multi-tenant)
Project to support multipathing in progress (802.1Qbp)
82nd IETF Taipei
<number>

## Slide 4: Use Cases
Point-to-Point Interconnection
  Use Ethernet or PPP encapsulated PW in IP/MPLS
  Use Ethernet or PPP mode on Bridge port at AC
  SPT Bridge and PE can be separate devices or one device
Multi-Site Interconnection
  Use PW mesh to interconnect SPT sites
  Can be full or partial mesh
82nd IETF Taipei
<number>

## Slide 5: Hierarchical L2VPN
SPT Bridge at low-tier network
IP/MPLS at top-tier network
Very scalable solution for L2VPN
82nd IETF Taipei
<number>

## Slide 6: Acknowledgement
Authors thank Donald Eastlake 3rd, Sue Hares, Sam Aldrin for their valuable contributions
82nd IETF Taipei
<number>

## Slide 7: Next Steps
Welcome the review and feedbacks
Proposal to add VPLS interconnection description
82nd IETF Taipei
<number>