## Slide 1: TRILL over MPLS draft-yong-trill-trill-o-mpls-00
82nd IETF Taipei
<number>
Lucy Yong lucy.yong@huawei.com
Donald Eastlake 3rd donald.eastlake@huawei.com
Sam.Aldrin sam.aldrin@huawei.com
John Hudson jon.hudson@brocade.com
Notes: <number>

## Slide 2: About This Draft
82nd IETF Taipei
<number>
Describes use cases for RBridge sites interconnected by an IP/MPLS network to form one RBridge campus using either:
  Point-to-Point TRILL Link
  Multiple Access TRILL Link
Introduce a new Hierarchical L2VPN architecture with RBridge and IP/MPLS
It is an informational draft because it requires no changes to the TRILL or MPLS standards

## Slide 3: Transparent Interconnect of Lots of Links (TRILL)
IETF base standard: RFC6325 and RFC6326
  Provide optimal pair-wise data frame forwarding with arbitrary topology and without configuration
  Supports multi-pathing for both unicast and multicast traffic
  Supports arbitrary link technologies
    Ethernet: RFC 6325
    PPP: RFC 6361
Devices implementing TRILL are called RBridges (Routing Bridges)
  Because they are IS-IS routers used to provide a transparent bridge-like service
RBridge Campus provides a bridged LAN service for connected customer bridges, end stations, or routers
82nd IETF Taipei
<number>

## Slide 4: Use Cases
Point-to-Point Interconnection
  Use Ethernet or PPP encapsulating PW in IP/MPLS
  Use Ethernet or PPP RBridge ports at AC
  PPP recommended for point-to-point as it saves ~16 bytes per frame
  RBridge and PE can be separated devices or one device
82nd IETF Taipei
<number>
<----------TRILL Link---------->
*-------* <----------PW----------> *-------*
| | AC +----+ +---+ +----+ AC | |
| RB +----| PE |----| P |---| PE |----+ RB |
|Site A | +----+ +---+ +----+ |Site B |
| | { PSN } | |
*-------* *-------*
{ One RBridge Campus }

## Slide 5: Use Cases
Multi-Access Link Interconnection
  Use MPLS/VPLS to provide a bridged LAN between RBridge ports at different sites
  TRILL supports Ethernet multi-access link (default mode)
82nd IETF Taipei
<number>
*-------* ........................... *-------*
| | . MPLS/VPLS . | |
| RB |AC +----+ PW +----+AC| RB |
| Site 1+---|VSI ********************** VSI|--+ Site 2|
| | | PE ***** ***** PE | | |
| | +----+ **** **** +----+ | |
| | . +*--*+ . *-------*
*-------* ..........|VSI |...........
| PE |
+----+
|AC
|
*---------*
| |
|RB Site 3|
| |
*---------*

## Slide 6: Hierarchical L2VPN
RBridges at low-tier network
IP/MPLS at top-tier network
Very scalable solution for L2VPN
82nd IETF Taipei
<number>
+---------+ ........................... +--------+
| | . IP/MPLS Core . | |
| | . . | +--
CE--+ |Eth+----+ PW +----+ | |
| RBridge +---| RB/|********************| RB/|--+RBridge |CEs
. --+ +-+ | PE |**** ****| PE |\ | +--
. | Site 1 | | +----+ **** **** +----+ -+ Site 2 |
. --+ | | . +*--*+ . | |
| | | ..........| RB/|........... +--------+
CE--+ | +--------------| PE |
| | Eth. Itfc +----+
+---------+ |Eth. Itfc
|
+---------+
| RBrdige |
| |
| Site 3 |
+-+----+--+
|... |
CEs

## Slide 7: Acknowledgement
Authors thank Ben Mack-Crane, Sue Hares, for their valuable contributions
82nd IETF Taipei
<number>

## Slide 8: Next Steps
Welcome the review and feedbacks
Work on auto-configuration for Hierarchical L2VPN
82nd IETF Taipei
<number>