## Slide 1: VPLS PE Model with E-Tree Support
<number>
82nd IETF - Taipei
Yuanlong Jiang (jiangyuanlong@huawei.com)
Lucy Yong (lucyyong@huawei.com)
Manuel Paul (manuel.paul@telekom.de)
Frederic Jounay (frederic.jounay@orange-ftgroup.com)
Florin Balus (florin.balus@alcatel-lucent.com)
Wim Henderickx (wim.henderickx@alcatel-lucent.com)
draft-jiang-l2vpn-vpls-etree-pe-05.txt
Notes: <number>

## Slide 2: Changes in draft-05
<number>
Add the support of PBB VPLS, so that we have two options for the support of S-tag access in E-Tree
  Either translate S-VLAN to another S-VLAN tag
  Or add a B-VLAN tag per PBB VPLS
For the support of E-Tree in H-VPLS, a new PE model is described in Appendix A.2
  Apply to both PW and Q-in-Q spoke
  Also compatible with E-NNI specification in MEF
Clarifications on the usage of tagged PW and raw PW mode, and a few other improvements on texts
82nd IETF - Taipei

## Slide 3: E-Tree Progress in Other SDOs
<number>
82nd IETF - Taipei
MEF
  Specifications for the E-Tree service: MEF 6.1, MEF 10.2
  Dual S-VLAN mechanism are required for an E-NNI with E-Tree support: MEF 26.1 draft, in progress
    E-Tree can be deployed across an arbitrary number of Operator MENs
IEEE
  Asymmetric VLAN is generalized to support E-Tree
ITU-T
  “Asymmetric VLANs" mechanism was incorporated in ITU-T G.8021, which was approved in Oct. 2010
All these SDOs are developing the E-Tree solutions fully compatible with the IEEE asymmetric VLAN mechanism
Notes: <number>
Why IETF develop a different E-Tree approach which is incompatible with the existing VPLS, and cannot interwork with other networks?

## Slide 4: Discussions
<number>
Three different approaches proposed for E-Tree support in VPLS hitherto
  Dual VLANs
  Dual PWs
  Control Word
Dual VLAN approach works in all scenarios, while the other two need extra workarounds or a redesign of the forwarding plane for the following use cases
  H-VPLS with Q-in-Q spoke per RFC 4762
  PE with multi-stage of bridge modules inside per RFC 6246
If asymmetric VLAN is supported in the bridge module within a PE, the dual VLAN solution is almost gratuitous for VPLS to support E-Tree
82nd IETF - Taipei
Notes: <number>

## Slide 5: Discussions (cont.)
<number>
When Access Circuit (AC) is untagged or tagged with C-VLAN tag
  VLAN based mechanism is quite simple
When AC is S-VLAN tagged
  This use case is still out of scope of both MEF and draft-l2vpn-vpls-etree-req
    S-VLAN is only required in E-NNI, not in UNI
  Two options are for the WG consideration
    S-VLAN translation
    Use of PBB VPLS
Do we really need any more options – dual flow labels, dual PWs, CW, etc.?
  More complexity in implementation and interworking
  More costs with doubtful benefits
82nd IETF - Taipei

## Slide 6: Questions
<number>
Solicit the consensus of the WG
Progressing as a WG draft?
82nd IETF - Taipei

## Slide 7
<number>
Thank You
82nd IETF - Taipei
Notes: <number>