## Slide 1: IS-IS VPLS for Data Center Network draft-xu-l2vpn-vpls-isis-02
Xiaohu Xu (xuxh@huawei.com)
Himanshu Shah (hshah@ciena.com)
IETF82, TAIWAN

## Slide 2: Cloud Data Center Network Requirements
Flat Layer 2 networking
  VM mobility requires extending the Layer2 domains across multiple PODs.
  Some cluster services also expect Layer2 connectivity.
Scalability
  Multi-tenancy capability (Beyond 4K VLANs).
  MAC table scalability (Millions of VMs within a data center) .
Maximize available bandwidth
  ECMP forwarding capability.
  Shortest path forwarding capability.
Fast convergence
  After network failure and VM move.
Simplified provisioning and operation

## Slide 3: Deploy VPLS in Data Center: Good News
VPLS could meet most requirements:
  Flat Layer 2 networking
  Scalability
    Multi-tenancy capability->adequate VPN instances.
    MAC table scalability->PBB+VPLS
  Maximize available bandwidth
    ECMP forwarding capability.
    Shortest path forwarding capability.
  Fast convergence
In addition, VPLS is a much proven L2VPN technology till now.

## Slide 4: Deploy VPLS in Data Center: Bad News
However, VPLS can’t meet the requirement of simplified provisioning and operation very well.
  Separate protocol(s) for VPLS (LDP and/or BGP)
  Full-mesh PWs
  VPLS peer configuration in LDP VPLS (w/o VPLS auto-discovery)
  BGP peer configuration in BGP VPLS or LDP VPLS (with VPLS auto-discovery)
    Image deploying PE at hundreds even thousands of ToRs within a single data center.

## Slide 5: Why not a Light-weight VPLS
Could the already deployed IGP (e.g., IS-IS) be extended a bit so as to deliver a light-weight VPLS which remains the advantages of VPLS while removing the shortcomings of VPLS?
  Flat Layer 2 networking 
  Scalability 
  Maximize available bandwidth 
  Fast convergence 
  Simplified provisioning and operation 
    No separate protocol(s) for VPLS
    No PWs
    No VPLS peer configuration
    No BGP peer configuration

## Slide 6: IS-IS TLV for VPLS

## Slide 7: VPLS Auto-discovery and Signaling
Auto-Discovery
  Each PE router could automatically discover which other PE routers are part of a given VPLS instance identified by the globally unique VPLS ID.
  PE router's configuration consists only of the identities of the VPLS instances established on this PE router, not the identities of any other PE routers belonging to that VPLS instance.
Signaling
  PE router assigns the same MPLS label for a given VPLS instance to any other PE routers.
  The VPLS label doesn’t need to be globally unique.

## Slide 8: Implications on the Control Plane
The extended IS-IS TLV for VPLS is partially transparent to P routers.
  P routers don't need to process the VPLS membership information contained in that IS-IS TLV, but only need to synchronize the Link State PDUs with their IS-IS neighbors.

## Slide 9: Implications on the Data Plane
Data encapsulation and data forwarding are not changed.
The only change is to the data-driven MAC learning:
  The VPLS label in the received VPLS packet is only intended to identify a given VPLS instance on the egress PE. Hence, the source IP address in the IP-based tunnel header should be resorted to identify the ingress PE of the received VPLS packet.
  Alternatively, MAC reachability could be distributed among PE routers on the control plane so as to eliminate unknown unicast flood.

## Slide 10: How to Deliver Mcast/Bcast/Unknown Unicast
Two options:
  Ingress Replication
    No state needed in the core, However, sub-optimal bandwidth utilization.
  P-Multicast Tree Mode
    Optimal bandwidth utilization. However, states required in the core.
Operators could make the tradeoff flexibly on basis of per tenant instance.

## Slide 11: How to Address the MAC Scalability Issue on PE Routers
PBB+VPLS
  PBB could be done at ToR switches or even at the servers.
  VPLS PE routers only need to learn B-MAC addresses.

## Slide 12: Comments