## Slide 1: Cloud Networking: Framework and VPN Applicability draft-bitar-datacenter-vpn-applicability-01.txt
Page - <number>
Nabil Bitar (Verizon)
Florin Balus, Marc Lasserre, and Wim Henderickx (Alcatel-Lucent) Ali Sajassi and Luyuan Fang (Cisco)
Yuichi Ikejiri (NTT Communications)
Mircea Pisica (BT)
November 2011
IETF-82, Taipei, Taiwan
Notes: <number>

## Slide 2: Scope
Page - <number>
Requirements for large scale multi-tenant data centers and cloud-networks
Applicability of existing and evolving Ethernet, L2VPN, and L3VPN technologies to multi-tenant cloud networking and tradedoffs:
  Intra-Data Center networks
  Inter-data center connectivity
    Data centers can belong to the same data center service provider, different data center providers, the tenant, and any hybrid
  Tenant and public access to data centers
Scenarios – cloud networks
Challenges/Gaps that still require work
Notes: <number>

## Slide 3: Cloud networking framework
DC GW – gateway to the outside world providing DC Interconnect and connectivity to Internet and VPN customers.
Core Switch/Router – high capacity core node, usually a cost effective Ethernet switch; may support routing capabilities.
ToR or Top of Rack – hardware-based Ethernet switch; may perform IP routing.
VSw or virtual switch – software based Ethernet switch running inside the server blades
IP/MPLS Network
Storage
DC
DC
FW
LB
VM-based Appliances
NAT
VMs on Server Blades
VM
VM
Customers with Application Requirements
VPN PEs/xGW
Multi-tenant Data Center
DC GW
Core
ToR
VSw

## Slide 4: Multi-Tenant Data Center and Data Center-Interconnect Requirements
Page - <number>
  Provide for network virtualization among tenants with overlapping addresses on the same data center network infrastructure – layer2 and layer3, and integrated routing and bridging
  Provide for compute and storage resources allocated to a tenant an attachment to the tenant virtual private network
  Provide connectivity between a tenant DC virtual infrastructure and the tenant sites, including tenant operated DCs
  Provide for dynamic stretching and shrinking of a tenant virtual infrastructure flexibly within a DC and across DCs
  Provide for DC operator virtual network management
DCGW2-2
DCGW1-1
DCGW2-1
ToR2
ToR1
SP IP/MPLS
Server Racks
Server Racks
DCGW1-2
DC1
DC2
L2/ L3
L2/ L3
L2/ L3
L2/ L3
PE
PE
VPN
VPN
PE
VPN
PE
VPN
Virtualization
Tenant 1
Site
Tenant 2
Site
Notes: <number>

## Slide 5: Multi-Tenant Data Center and Data Center-Interconnect Requirements
Page - <number>
Support large Scale DCs :
  Large number of tenants – a tenant identified by a service ID in data plane and/or control plane.(e.g., >> 4K VLAN IDs)
  Large number of VMs and multiple per-VM virtual NICs  large number of Ethernet MACs, IP addresses and ARP entries that need to be accommodated in the data center network infrastructure
  Multicast and broadcast containment per tenant virtual domain to conserve bandwidth resources
  VM movement and network rapid convergence in the presence of a large number of tenants and VMs
Optimize network resource utilization
  Bandwidth utilization within data center, on the DC connection to the WAN, and across the WAN
  FIB utilization at routers and switches
  Control plane resource utilization on routers and switches
Notes: <number>

## Slide 6: Multi-Tenant Data Center and Data Center-Interconnect Requirements
Page - <number>
Path Optimization
  Provide for optimized forwarding – shortest path between any two communicating endpoints in a virtual network to improve latency and network utilization efficiency
  Eliminate or reduce traffic black-holing when a VM is moved from one location to another during network transition – traffic redirection until convergence to shortest path
Resiliency: Fast recovery around failure
VM Mobility
  Maintain the existing client sessions upon VM move: VM keeps the same IP and MAC address
  Expand/shrink L2/L3 domains within a DC and across DCs
  Optimal traffic forwarding: shortest path, avoid triangular routing in steady state and provide for traffic redirection during transition
  Rewrite the MAC FIBs to redirect traffic to new location
  Have a VM IP route where needed to direct traffic to the VM
Notes: <number>

## Slide 7: Multi-Tenant Data Center and Data Center-Interconnect Requirements
Page - <number>
Auto-discovery by the network of a VM location with minimal network configuration touches – cater to ease of management
Support for OAM to troubleshoot connectivity problems and provide for SLAs at the service layer (layer2 or layer3)
Ease of introduction of new DC networking technologies in existing DC environments
Allow for the following networking models
  DC service provider and the WAN network service provider providing access to a tenant site are two different entities.
  DC service provider and the WAN network service provider providing access to a tenant site are same entities
  DC can have its own private network for its own data center connectivity or can use another network service provider
Notes: <number>

## Slide 8: VPN applicability to Cloud Networking
Layer 3 option
  e.g. RFC4364
Layer 2 options
  VLANs and L2VPN toolset
  PBB and L2VPN toolset
  TRILL and L2VPN toolset
  In current draft version, PBB with L2VPN options have been detailed

## Slide 9: Addressing L3 virtualization with IP VPNs
Use full fledge IP VPN for L3 Virtualization inside a DC
IP VPN advantages
  Interoperates with existing WAN VPN technology
  Deployment tested, provides a full networking toolset
  Scalable core routing – only one BGP-MP routing instance is required compared with one per customer/tenant in the Virtual Routing case
  Service Auto-discovery - automatic discovery and route distribution between related service instances
  Well defined and deployed Inter-Provider/Inter-AS models
  Supports a variety of VRF-to-VRF tunneling options accommodating different operational models: MPLS [RFC4364], IP or GRE [RFC4797]
Connectivity models for customer IP VPN instances located in the WAN
  DC GW may participate directly in the WAN IP VPN
  Inter-AS Options A, B or C - applicability to both Intra and Inter-Provider use cases

## Slide 10: PBB + L2VPN applicability to Cloud Networking
24b ISID tag vs. 12b VLAN tag used for Tenant identification
  Expands L2 domains from 4K VLANs to 16M ISIDs
  Standardized in 2008 by IEEE – inherits current and future IEEE specs (QoS, OAM, control plane etc…)
  Supported in merchant silicon, proven vendor interoperability
  Deployed in a number of large service provider networks
ISID tag follows the VLAN tag format
  I-Tag code point implies the presence of (VM) MAC DA, SA right after I-SID
12b VLAN
4b QoS
24b I-SID
4b QoS
4b RSV
versus
Ethertype (16b)
Ethertype (16b)

## Slide 11: Supported tunneling options for 24b ISID Tag
WAN: Inter-DC, VPN connectivity 24b I-SID tag over MPLS
DC GW
DC
DC GW
24b I-SID tag over native Ethernet tunneling
DC GW
DC
DC GW
24b I-SID tag over
IP tunneling
  Native Ethernet – IEEE 802.1ah-2008
  Ethernet over IP (L2TPv3) or MPLS tunneling - PBB-VPLS
  Other more optimized IP tunneling options could be explored
DC GW
DC
DC GW
24b I-SID tag over
MPLS

## Slide 12: VPN interoperability w/ PBB+L2VPN IP VPN Example
DCGW2-1
DCGW2-2
ToR2
ToR1
PE
WAN IP/MPLS
PE
Server Racks
Server Racks
DCGW1-2
DCGW1-1
DC1
DC2
IP- VPN
IP- VPN
ISID-tags
I-SID tags
I-SID ELAN
I-SID ELAN
PE
IP- VPN
IP- VPN
PE
PE
PE
IP- VPN
IP- VPN
I-SID ELAN
I-SID ELAN
IP- VPN
IP- VPN
PBB I-SID tag termination into IP VPN VRFs: from IP over VLAN to IP over I-SID interfaces
  Same tunneling options: Native Ethernet, IP or MPLS or a mix

## Slide 13: VPN interoperability w/ PBB+L2VPN Example
DCGW2-1
DCGW2-2
ToR2
ToR1
WAN IP/MPLS
Server Racks
Server Racks
DCGW1-2
DCGW1-1
PBB VPLS
PBB VPLS
PBB VPLS
PBB VPLS
PE
PE
PE
PE
PE
PE
VPLS
VPLS
VPLS
VPLS
Option1: PBB I-SID termination into PBB-VPLS
  DCGW translates back to regular VPLS
Option2: PBB I-SID transparently transported over PBB-VPLS
  DCGW acts as a Backbone Core Bridge: no ISID provisioning, no VM MAC awareness
Same tunneling options available: Ethernet or IP or MPLS or a mix
I-SID ELAN
I-SID ELAN
I-SID ELAN
I-SID ELAN
DC1
DC2
ISID-tags
I-SID tags

## Slide 14: VLAN interoperability w/ PBB+L2VPN
DCGW2-1
DCGW2-2
ToR2
ToR1
PE
WAN IP/MPLS
PE
Server Racks
Server Racks
DCGW1-2
DCGW1-1
PE
PE
PE
PE
PBB- VPLS
PBB- VPLS
Similarly with VPLS interop, DCGWs in DC1 translate PBB I-SIDs to VPLS
  Alternatively DCGWs in DC2 may run PBB-VPLS and translate I-SIDs to VLANs
I-SID ELAN
I-SID ELAN
VLAN ELAN
VLAN ELAN
DC1
DC2
ISID-tags
Ethernet VLANs
VPLS
VPLS
VPLS
VPLS

## Slide 15: PBB and L2VPN - control plane options
WAN: Inter-DC, VPN connectivity 24b I-SID tag over MPLS
DC GW
DC
DC GW
24b I-SID tag over native Ethernet tunneling
DC GW
DC
DC GW
24b I-SID tag over
IP tunneling
DC GW
DC
DC GW
24b I-SID tag over
MPLS
Legacy: STP, MC-LAG
Nextgen: IS-IS (SPB)
Regular IP Routing
Regular IP Routing, MPLS toolset
Legacy: PW Mesh with split horizon
Nextgen: BGP (PBB-EVPN)

## Slide 16: PBB and L2VPN - control plane options
Re-use of IP Routing toolset: IS-IS, BGP based control plane choices
Service Auto-discovery, minimize operator provisioning
  Hypervisor to ToR VM discovery methods: VDP (IEEE 802.1Qbg), IGMP, SDN, others
Supports L2 multipathing and Active/Active Multihoming
Fast convergence, Traffic Steering
Inter-AS expansion with BGP

## Slide 17: Other work in progress
Discussion on VM Mobility, Optimal traffic forwarding – see draft-raggarwa-data-center-mobility-01.txt
ARP suppression discussed in PBB-EVPN (draft-sajassi-l2vpn-pbb-evpn-02.txt) and EVPN (draft-raggarwa-sajassi-l2vpn-evpn-04.txt)
ARP Broadcast Reduction for Large Data Centers (draft-shah-armd-arp-reduction-02.txt )

## Slide 18: PBB+L2VPN Solution Summary
Draft Component | PBB+L2VPN toolset
Tenant ID | 24b tag
Tag format | IEEE 802.1ah I-SID
VM MAC hiding | Yes
Tunneling options | IP, MPLS, Ethernet
IP tunnel format | PW/L2TPv3
IP core routing | Yes

## Slide 19: PBB+L2VPN and DC Challenges
Draft Requirements | VPN Applicability
Service Scale | Yes (16M)
MAC scale | Yes (overlay)
Flood containment | Yes (Ethernet, MPLS) TBD for IP overlay
Convergence, Multi-pathing | Yes (IS-IS, BGP)
Multicast efficiency | P2MP LSPs, TBD (IP)
VPN Interop | Yes
VM Mobility | Work in progress

## Slide 20: Next steps
  Potential work items
    IP tunneling optimization for I-SID tag transport
    Network auto-provisioning and flood containment through the auto-discovery of VM and VM groups: agree on mechanism(s)
    Broadcast, Multicast handling over IP Core requires work
    Tunnel and Service Address Translation between Cloud Provider and Tenant/Network Service Provider