## Slide 1: Extensions to RSVP-TE for P2MP LSP Ingress/Egress Local Protection
draft-chen-mpls-p2mp-ingress-protection
draft-chen-mpls-p2mp-egress-protection
Huaimo Chen (huaimochen@huawei.com)
Ning So (Ning.So@verizonbusiness.com)
Autumn Liu (autumn.liu@ericsson.com)

## Slide 2: Contents
Ingress/Egress Local Protection with FRR
Advantages of Ingress/Egress Local Protection
MVPN over P2MP LSP with Protection

## Slide 3: Ingress/Egress Local Protection with FRR
Ingress of P2MP LSP is locally protected (New)
Every egress of P2MP LSP is locally protected (New)
Every link and intermediate node of P2MP LSP is locally protected using FRR (Existing)
Thus
All parts of P2MP LSP are locally protected

## Slide 4: P2MP LSP Ingress & Egress Local Protection(Animated)
P2MP
Multicast
Source
Multicast
Receiver
Data
PE6
PE5
PE4
PE3
CE4
CE3
CE2
CE1
One P2MP LSP for all: Every part (ingress & egress) is locally protected
Big resource saving (e.g, no double bw resv)
Faster failure recovery: local protection speed
P2MP LSP
Backup LSP
Data
PE1
PE2
CE1
(S,G)Join
BFD
Existing scenario: double root and every leaf
Create two global P2MP LSP from each root to leaves, carrying data at same time
BFD

## Slide 5: Advantages of P2MP LSP Ingress/Egress Local Protection
All parts of P2MP LSP are locally protected
Only one P2MP LSP is used to implement an E2E protection
  Normally two P2MP LSPs are used
Big saving on resource : 50% bandwidth saving
  No need to reserve/use double bandwidth
Faster recovery
  Speed of local protection recovery
  Flow recovery within 50ms when a failure happens
Easier to operate

## Slide 6: MVPN over P2MP LSP with Protection (Animated)
<number>
P2MP
Data
PE6
PE5
PE4
PE3
CE4
CE5
CE3
VNP related behavior:
VPN Label put inside label stack in (backup) ingress (PE5/PE6)
VPN Label used for forwarding in (backup) egress (PE1/PE2)
P2MP LSP
Backup LSP
Data
PE1
PE2
CE1
(S,G)Join
BFD
Ingress/Egress Locally Protected
Link, middle node protected by FRR
BFD
VPN A Site 1
VPN B Site 1
VPN A Site 2
VPN B Site 3
CE2
VPN A Site 3
VPN B Site 2
CE6
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 7: Next Step
Welcome comments
Request to make it into a working group document

## Slide 8: P2MP LSP Ingress Local Protection (Animated) -- Backup LSP Depends on Primary LSP
<number>
P2MP
Multicast
Source
Multicast
Receiver
Data
Data
PE1
PE2
PE6
PE5
PE4
PE3
CE4
CE3
CE2
CE1
P2MP LSP
Backup LSP
Connection for BFD
BFD
PE6 updates Backup LSP when PE5 works and P2MP LSP changes
Primary ingress PE5 works:
New branch added to P2MP LSP
PE6 adds a branch to Backup LSP
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 9: P2MP LSP Ingress Local Protection (Animated) -- Backup LSP Is Solid When Failure Happens
<number>
P2MP
Multicast
Source
Multicast
Receiver
Data
Data
PE1
PE2
PE6
PE5
PE4
PE3
CE4
CE3
CE2
CE1
Primary ingress PE5 fails:
Traffic to backup tunnel
Traffic merged into P2MP LSP
PE6 keeps Backup LSP
P2MP LSP
Backup LSP
Connection for BFD
BFD
PE6 keeps Backup LSP when PE5 fails
Notes: <number>
<footer>
<header>
<date/time>
<number>