## Slide 1: Support for RSVP-TE in L3VPNs draft-kumaki-murai-l3vpn-rsvp-te-04.txt
Kenji Kumaki KDDI Corporation
Tomoki Murai Furukawa Network Solution Corp.
Dean Cheng Huawei Technologies
Satoru Matsushima Softbank Telecom
Peng Jiang KDDI R&D Labs
November 2011
82th IETF@Taipei
Notes: <number>

## Slide 2: Brief Recap 1/3 (Motivation)
Aggregation for VPNs over RSVP-TE
Service Providers will provide customer LSPs in BGP/MPLS VPNs.
  Requirements for Supporting Customer Resource ReSerVation Protocol (RSVP) and RSVP Traffic Engineering (RSVP-TE) over a BGP/MPLS IP-VPN
    RFC 5824
It is necessary that RSVP control messages, such as Path messages and Resv messages, are appropriately handled by PE routers.
Our goal is to establish an end-to-end MPLS TE LSP between customer sites.
82th IETF@Taipei
November 2011
Notes: <number>

## Slide 3
Brief Recap 2/3 (Problem Statement)
BGP/MPLS
IP-VPN
CE
CE
CE
CE
PE 1
VPN 1
VPN 1
VPN 2
VPN 2
VPN 2: MPLS TE LSPs
VPN 1: MPLS TE LSPs
PE 2
?
?
Path message
Resv message
The PE2 can’t identify Path messages between the VPN1 and the VPN2 when it sends them to the same destination.
The PE1 can’t identify Resv messages between the VPN1 and the VPN2 when it sends them to the same destination.
Need to extend from current specification (RFC 3209).
82th IETF@Taipei
November 2011
Notes: <number>

## Slide 4: Brief Recap 3/3 (Solution)
Define the new object types
  LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 SESSION Object
  LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 SENDER_TEMPLATE Object
  LSP_TUNNEL_VPN-IPv4 / LSP_TUNNEL_VPN-IPv6 FILTER_SPEC Object
Very simple minimal extension which is backward compatible
82th IETF@Taipei
November 2011
Notes: <number>

## Slide 5
Related drafts
Submit to PCE WG
  PCEP extensions for a BGP/MPLS IP-VPN
    draft-kumaki-murai-pce-pcep-extension-l3vpn-08
82th IETF@Taipei
November 2011
The PCE architecture is the most suitable to calculate MPLS TE LSPs between BGP/MPLS IP-VPN sites
Notes: <number>

## Slide 6
Recent Updates
Support from Huawei and Softbank
Furukawa Implemented
Updated text for clarity and readability
  Cleaned up the abstract
  Rewrote some of the introduction text to clarify application and intention of the document
  Clarified motivation and network example
  Various edits and nits
82th IETF@Taipei
November 2011
Notes: <number>

## Slide 7
Next Steps
Need more comments and feedback from WG
Request WG to accept this I-D as a WG document
Poll WG for interest
82th IETF@Taipei
November 2011
Notes: <number>
Rename the title of this I-D to better describe the contents inside