## Slide 1: draft-yue-mmusic-rtsp-substream-control-extension
Peiyu YUE (Roy)
Huawei Technologies

## Slide 2: Scenario: Single Session Transport --- used for SVC and MVC
Server
RTSP+RTP
Client
RTSP+RTP
Single RTP Session
base layer
enhancement layer 1
enhancement layer 2
Example :SVC content transport to client
Problem identified:
How can the client retrieve part of the content (e.g. Operation point 1, the base layer), or even switch between operation points?
Operation point 1:
Operation point 2: +
Operation point 3: + +

## Slide 3: Definition
Definition
  Substream: a part of a media stream containing one or more bitstream components, which can be independently decoded.
  Typically a Substream is identified by an operation point.
  Substream type: the compound mode of the bitstream components in a substream, e.g. SVC, MVC, etc

## Slide 4: Substream control solution
Annotation
  Signaling the substreams available for control.
  It is usually done by the SDP specification of the RTP PF specification
Capability negotiation
  Based on the RTSP feature tag negotiation mechanism
  new feature tag defined
Control operations
  Define new RTSP header, used in PLAY request.
  New status code for failure cases

## Slide 5: Example
Server
Client
SDP:
…….
m=video 20000 RTP/AVP 97
a=rtpmap:97 H264-SVC/90000
a=fmtp:97 profile-level-id=53000c; packetization-mode=1;
sprop-parameter-sets={sps0},{sps1},{pps0},{pps1};
sprop-operation-point-info=<1,0,0,0,4de00a,3200,176,144,128,
256>,<2,1,1,0,53000c,6400,352,288,256,512>;
SDP
RTSP SETUP
200 OK
RTSP PLAY
200 OK
PLAY rtsp://example.com/svc.mp4/ RTSP/2.0
CSeq: 6
User-Agent: PhonyClient/1.2
Range: npt=30.87-634.10
Seek-Style: Next
Session: 12345678
Substream: rtsp://example.com/svc.mp4/, SVC, lay-id=1
SETUP rtsp://example.com/SVC.mp4/ RTSP/2.0
CSeq: 3
User-Agent: PhonyClient/1.2
Require: play.substream
Transport: ……

## Slide 6: Summary of extensions
Extension to RTSP
  Header extension:
    Substream, contains the Request-URI, substream type and substream id triples.
  Feature Tag extension
    Play.substream, indicating the support of substream control defined here.
  Status Code Extension
    552 Substream Type Not Recognized
    553 Substream Control Not Allowed
    554 Substream Id Not Valid

## Slide 7: Next step
Complete the MVC part with the ongoing discussion of I-D.ietf-payload-rtp-mvc
  MVC substream annotation
  MVC substream id
Discuss on the need of in-band signaling of substream annotation.
  e.g. when the client request to play a non-exist substream, 554 error will be responded. In this response message, the substream annotation may be further contained. Does this make sense?
Security considerations?