## Slide 1: Miscellaneous Capabilities Negotiation in SDP
IETF82 Taipei, Taiwan
Simo Veikkolainen
simo.veikkolainen@nokia.com

## Slide 2: The use case
Alice
Bob
“I’ll offer PSTN audio, but can also do RTP audio”
“Let’s use RTP audio”
ICE is not an option for PSTN – SDP capability negotiation needed for alternative media
draft-ietf-mmusic-sdp-cs states the port number for circuit-switched media is 9 (the “discard” port)
UDP port selected for RTP media

## Slide 3: Alternative port numbers
SDP Capability Negotiation or its extensions do not currently enable offering alternative port numbers
Options
  Circuit-switched media uses the same port as RTP media – even though the port is not really used
  Extend capneg with a “port capability” attribute, restricting its use to cases where ICE can’t be used