## Slide 1: Return Path Specified LSP Ping
draft-ietf-mpls-return-path-specified-lsp-ping-04.txt
Mach Chen (mach@huawei.com)
Ning So (ning.so@verizonbusiness.com)
Wei Cao (caowayne@huawei.com)
Fredric Jounay (frederic.jounay@orange-ftgroup.com)
Simon Delord (simon.delord@gmail.com)
IETF 82h MPLS WG Taipei

## Slide 2: Return Path Specified LSP Ping Overview
Specify the return path of the echo reply in the echo request message, by
  Introduce a new reply mode: Reply via specified return path (5)
  Define a new TLV: Reply Path TLV, identify the specified return path
Echo reply is extended to test the return path
  By carrying the FEC stack information of the return path
  Both directions of a bidirectional LSP tested by a single LSP Ping message exchange
IETF 82h MPLS WG Taipei

## Slide 3: The changes from 03->04
The draft is quite stable
The changes mainly on IANA consideration (see next slides)
Editorial changes
IETF 82h MPLS WG Taipei

## Slide 4: The changes from 03->04 (cont.)
Version 03
  Apply existing sub-TLVs of Target FEC Stack TLV to Reply Path TLV
  Reply Path TLV has its own “TLV and sub-TLVs” registry and sub-registry
Version 04
  Expect to apply all existing and future defined sub-TLVs of Target FEC Stack TLV to Reply Path TLV
    Share the registry and sub-registry with Target FEC Stack TLV
    But how to register the dedicated sub-TLVs to Reply Path TLV?
      Re-define the “Vender Private” range?
        For Target FEC Stack TLV, it is still the “Vender Private” range,
        but for other TLVs, it is treated as a normal number space
      Or, reserve/allocate a TLV-unique range (e.g., starting from 1024)?
        The number spaces split into two part: Common to all TLVs and TLV-unique
IETF 82h MPLS WG Taipei
Notes: <number>

## Slide 5: Next steps
Address the comments raised on the list
  Especially the IANA issue
Submit a new version and ask for WG last call
IETF 82h MPLS WG Taipei

## Slide 6
Thanks!
IETF 82h MPLS WG Taipei