## Slide 1
MPLS-TP
Next-Hop Ethernet Addressing
draft-fbb-mpls-tp-ethernet-addressing-00
Dan Frost danfrost@cisco.com
Stewart Bryant stbryant@cisco.com
Matthew Bocci matthew.bocci@alcatel-lucent.com
IETF 82
November 2011
MPLS

## Slide 2
The Ethernet Addressing Problem
No standard answer to this basic question
Some implementations using broadcast address or relying on static MAC configuration; both have problems
Considerations differ for point-to-point vs. multipoint Ethernet links
In an MPLS-TP network without IP, how do you determine the Ethernet MAC address of the next hop?

## Slide 3
Solution
This draft mainly consists of text that was originally part of the MPLS-TP Data Plane Architecture (RFC 5960) and accepted by the WG, but which was taken out for scope reasons
A reserved Ethernet multicast address is allocated and dedicated for MPLS-TP point-to-point links
Use of static addressing and broadcast address still allowed, but multicast address SHOULD be used instead and MUST be supported by default in the receive path
Draft also defines an Ethernet data-set for the G-ACh Advertisement Protocol that enables unicast MAC discovery even without IP

## Slide 4
Next Steps
Recommend WG adoption to resolve this open issue and get an early multicast address allocation as MPLS-TP implementations near completion
82