## Slide 1: LSP Ping extensions for echo reply relay draft-zj-mpls-lsp-ping-reply-relay-00
Ryan Zheng
Lizhong Jin
IETF 82 - Taipei
<number>
Notes: <number>

## Slide 2
Inter-area scenario in Seamless MPLS
P nodes would be unable to respond for the lack of IP reachable route to ANs.
draft-ietf-mpls-interas-lspping addresses similar problem, but only for inter-AS scenarios.
Better to have a generic solution.
Discard
LSP
Echo request
Motivation
<number>
Notes: <number>

## Slide 3: Introduction
IETF 82 - Taipei
Extends a new Routable Relay Node Address TLV for the LSP Ping mechanism.
The replying LSR would send the echo reply to a routable node indicated by the new TLV.
The echo reply would be relayed to the initiator finally.
<number>

## Slide 4: Routable Relay Node Address TLV
IETF 82 - Taipei
Carried in echo request and echo reply message
<number>

## Slide 5: An Example
This is an example to show the address list in each reply message.
The echo reply sent by P would be relayed by ABR1, then to AN1.
<number>

## Slide 6: Next Steps
Updated to version-01
  addresses the UDP port issue
<number>

## Slide 7: Next Steps
IETF 82 - Taipei
Updated to version-01
  adds the Security Considerations
Merged with draft-ietf-mpls-interas-lspping?
Seeking feedback from WG
<number>