## Slide 1: Protection Mechanisms for LDP P2MP/MP2MP LSP
82nd IETF @ Taipei
draft-zhao-mpls-mldp-protections-00.txt
Quintin Zhao, Emily Chen, Huawei

## Slide 2: Motivations and Scope of the Draft
82nd IETF @ Taipei
Motivations:
  The number of service providers to deploy real-time multicast applications using Multicast LDP (mLDP) across MPLS networks is increasing.
  There is a clear need to protect these real-time applications and to provide the shortest switching times in the event of failure.
The scope of this document
  outlines the requirements,
  describes the protection mechanisms available,
  Propose the necessary extensions to facilitate mLDP P2MP and MP2MP LSP protection within an MPLS network.

## Slide 3: Requirements
82nd IETF @ Taipei
  A number of requirements have been identified that allow the optimal set of mechanisms to developed. These currently include:
    Computation of a disjointed (link and node) backup path within the multicast tree;
    Minimization of protection convergence time;
    Optimization of bandwidth usage.

## Slide 4
There is no existing automatically signaled protection solution for the node failure using a P2P backup LSP in mLDP
R2
R6
R4
R5
R1
Root
Receiver
Receiver
R3
<number>
mLDPfRRoP2P Problem Statement

## Slide 5
<number>
Protect the specific node or link with P2P backup LSP in mLDP
R2 send notification message (or extend the label mapping ) to R3 and tells R3 that R2 has two downstream nodes, R1 and R4 with forwarding labels L21 and L24 respectively.
When R3 sees R2 node or link going down, it takes mLDP packet as it would send it to R1 and R4 through R2 and sends it into the two p2p backup tunnels :
  Tunnel Red : R3->R6->R5->R4 using inner label L21;
  Tunnel Blue: R3->R6->R5->R4->R1 using Inner label L24;
PHP in R5 for tunnel Red and in R4 for tunnel Blue will cause backup tunnel labels to be removed;
R1 will receive same packets as from the interface between R2 and R1 , just from different interface same forwarding !
R4 will receive same packets as from the interface between R2 and R4 , just from different interface same forwarding !
R2
R6
R3
R4
R5
R1
Root
Receiver
Receiver
Label L21
Label L24
L21
Label L32
L21+L36
L24+L36
L21+L65;
L21+L54;
L24+L65
L24
mLDPfRRoP2P Solution
notification message

## Slide 6: mLDPfRRoP2P Protocol Extension
82nd IETF @ Taipei
A new type of LDP MP Status Value Element is introduced for notifying downstream LSRs and respective labels. It is encoded as follows:
The Downstream Element is encoded as follows:

## Slide 7: mLDPfRRoP2MP Problem Statement
82nd IETF @ Taipei
When the downstream of the protected node has more branches,
using mLDPfRRoP2p means a lot of duplicated p2p tunnels.
Many duplicates here
Leaf PE
Sender PE
P1
Sender PE
P2
Leaf PE
Leaf PE
Leaf PE

## Slide 8: mLDPfRRoP2MP Solution
82nd IETF @ Taipei
In the example above, p1 has downstream branch node p3, p4, p5 and p6. To protect the P2 node, the PLR node needs set up a p2mp bypass path through p2 to reach the p3, p4, p5, and p6 nodes.
To build the bypass path, p1 needs to signal P3, p4, p5 and p6 the upstream router PLR info and then these nodes will send the label mapping messages to PLR through the alternate route, In this example, it is the p2 node.
Leaf PE
Sender PE
Leaf PE
Leaf PE
Leaf PE
P1
P2
P3
P4
P5
P6
PLR

## Slide 9: mLDPe2eFRR Problem Statement
82nd IETF @ Taipei
How can we setup disjointed LSPs where the two LSP paths
share the same Routing tables?

## Slide 10: mLDPe2eFRR Solution
82nd IETF @ Taipei
The draft of ietf-mpls-ldp-multi-topology provides a mechanism
to setup disjointed LSPs within different topologies.
In the example above, Leaf 1 and Leaf 2 may trigger mLDP LSPs in different topologies,
sending label mapping messages with same FEC element, different MT-ID and different label.
When the Root node receives the label mapping messages from different topologies, it will
set up two mLDP LSPs for application as end-to- end protection.

## Slide 11: Next Steps
82nd IETF @ Taipei
The authors will update the draft to include the details of:
  the mLDPfRRoP2MP solution;
The authors will update the draft to include the discussion of:
  head end node protection;
  leaf node protection
The authors request WG experts to review and comment on each protection solutions.

## Slide 12: Questions & Comments?
82nd IETF @ Taipei

## Slide 13: Thanks!
82nd IETF @ Taipei