## Slide 1: MPLS-TP Protection For Interconnected-ring draft-liu-mpls-tp-interconnected-ring-protection
Guoman Liu ( liu.guoman@zte.com.cn )
Weingarten Yaacov ( Yaacov.weingarten@nsn.com )
82th IETF Meeting in Taipei
Notes: <number>

## Slide 2: Motivation
Requirement from RFC5654
  Req.93 : when a network is constructed from interconnected rings, MPLS-TP MUST support recovery mechanisms that protect user data that traverses more than one ring.
Purpose of this draft
  This draft describes all kinds of interconnected ring scenarios and provides a few protection solutions for the multi-ring service that traverse more than one ring.
Notes: <number>

## Slide 3: Dual-node interconnection
For the interconnection scenario, it may use 1:1 linear protection to recovery the failure of interconnection link . In addition, it still may set up end to end protection path which traverse ring 1 and ring 2 to recovery the multi-ring service ;
C
B
A
D
E
F
6
1
2
5
4
3
interconnection link
ring 1
ring 2
Notes: <number>

## Slide 4: Single-node interconnection
As the interconnection node( eg. Node A ) is only a single point that connect two ring , when the failure happens on the interconnection node, the multi-ring service may not be recovery, so the scenario should be avoided.
C
B
A
D
E
1
2
4
3
ring 1
ring 2
Notes: <number>

## Slide 5: chained interconnection
For the interconnection scenario, when interconnection node( node A or node F) or link(A-F) has the failure , it may set up end to end protection path which traverse ring 1 and ring 2 to recovery the multi-ring service.
C
B
A
D
E
F
1
2
4
3
chained link
ring 1
ring 2
Notes: <number>

## Slide 6: Dual-node and single-node interconnection
For the mixed interconnection, it may separately use recovery mechanism of dual-node or single-node interconnection to recovery the failure between any two directly connected-ring. In addition, it still may set up end to end protection path which traverse ring 1,ring 2 and ring 3 to recovery the multi-ring service .
C
B
A
D
E
F
6
1
2
5
3
interconnection link
ring 1
ring 2
ring 3
Notes: <number>

## Slide 7: Dual-node and chained interconnection
For the mixed interconnection, it may separately use recovery mechanism of dual-node or chained interconnection to recovery the failure between any two directly connected-ring. In addition, it still may set up end to end protection path which traverse ring 1,ring 2 and ring 3 to recovery the multi-ring service .
C
B
A
D
E
F
6
1
2
5
4
3
interconnection link
ring 1
ring 2
ring 3
Notes: <number>

## Slide 8: chained and single-node interconnection
For the mixed interconnection, it may separately use recovery mechanism of single-node or chained interconnection to recovery the failure between any two directly connected-ring. In addition, it still may set up end to end protection path which traverse ring 1,ring 2 and ring 3 to recovery the multi-ring service.
C
B
A
D
E
F
6
1
2
5
3
interconnection link
ring 1
ring 2
ring 3
Notes: <number>

## Slide 9: Chained,dual-node ,single-node interconnection
For the mixed interconnection, it may separately use recovery mechanism of dual-node or chained ,single-node interconnection to recovery the failure between any two directly connected-ring. In addition, it still may set up end to end protection path which traverse ring 1,ring 2 ,ring 3 and ring 4 to recovery the multi-ring service.
C
B
A
D
E
F
6
1
2
5
3
interconnection link
ring 1
ring 2
ring 3
ring 4
Notes: <number>

## Slide 10: Next steps
complete the part of recovery mechanism in the next version;
update the document according to comments of the meeting and Mailing list.
thank you !
Notes: <number>