## Slide 1: Multicast LDP extension for hub & spoke multipoint LSP
draft-jin-jounay-mpls-mldp-hsmp-04
Lizhong Jin
Frederic Jounay
IJsbrand Wijnands
Nicolai Leymann
<number>
MPLS IETF82
Notes: <number>

## Slide 2: Update
Have presentation on IETF79 Beijing meeting.
Update section 2: Application.
<number>

## Slide 3: Applications
Time synchronization based on [IEEE1588v2].
Typical IPTV scenario could use HSMP LSP for multicast.
P2MP PW with reverse path can multiplex to HSMP LSP.
Newly added application:
  VPLS implementation with P2MP PW multiplexed to HSMP LSP.
<number>

## Slide 4: Applications (cont)
VPLS implementation scenario:
  Each P2MP PW is multiplexed to HSMP LSP.
  Each PE signals a P2MP PW with itself as a root to all other PEs in the VPLS.
  All broadcast/multicast/unknown traffic from this PE will use this P2MP PW.
  Unicast traffic from a particular PE to another PE will be sent from leaf to root using the reverse path of P2MP PW.
  Advantage:
    Reducing traffic utilization from broadcast, multicast and unknown traffic;
    Reducing the total number of LSPs maintained by each PE (i.e. instead of requiring a full mesh of PW, now only require one P2MP PW multiplexed to HSMP per PE).
<number>

## Slide 5: Next steps
Ask WG to adopt this draft.
Thank you
<number>