## Slide 1: Support Shared Mesh Protection in MPLS-TP
IETF 82
November 13, 2011
Ping Pan, Rajan Rao, Biao Lu (Infinera)
Fatai Zhang, Sam Aldrin (Huawei)
Luyuan Fang (Cisco)
Andrew G. Malis (Verizon)
Fei Zhang (ZTE)
Mohana Singamsetty (Tellabs)

## Slide 2: What is Shared Mesh Protection? (Required per MPLS-TP Requirements (Req 68, 69, RFC5654))
The resources on P-Q-R is shared
by multiple working LSP’s
Key properties:
  Protecting LSP’s are pre-established
  Upon failure, a working LSP needs to activate the protection
  And, it may preempt/notify other connections
  If the resources are taken, it needs to try another protecting LSP (1:N)

## Slide 3: Protocol Operation Overview
A
B
C
D
E
F
G
Working LSP
4. Activation
4. Activation
4. Activation
4. Activation
1. Setup a protecting connection
2. Setup HW
2. Setup HW
2. Setup HW
2. Setup HW
2. Setup HW
3. Failure
Request: SF/SD/FS/EXER/… R: Revertive Status: OK/failure Seq: reliable messaging

## Slide 4: Key Function and Major Changes since Last IETF
Operation in Summary
  Activation
  De-activation
  Query
  Pre-emption
Major Changes
  Adapted the PSC Logic from RFC 6378 (Linear Protection)
  Simplified the protocol message format
  Consolidated with G.SMP work in ITU (same protocol procedure can apply in both packet and circuit networks)
Collaboration Status
  Consolidated with all outstanding proposals, except one
  The only remaining issue: the need for reliable message delivery
Next Step
  Ready to advance to Working Group document