## Slide 1: draft-ietf-mpls-entropy-label
ietf 82

## Slide 2: Entropy Labels
Generalize what’s been done in the fat PW draft
  Define general characteristics of entropy labels
  Define the Entropy Label Indicator label: what, why, how used, etc.
  Define signaling and forwarding behavior for RSVP-TE and LDP tunnels and for labeled BGP
  Define signaling for other applications: IP VPNs, VPLS, IP over MPLS, etc.

## Slide 3: Draft Changes 00 to 01
Removed wording that entropy label MUST be at bottom of stack (see later) (cf RFC 4182)
  For completeness, added verbiage for CoS bits
Changed requirement of TTL value on ELI from 1 to TTL of label above in the stack
Tightened up EL processing on ingress, transit and egress LSRs

## Slide 4: Draft Status
Stable
  So, let’s mess with it :-)
So, here are some things to think about:
  Does the entropy label have to be at the bottom of stack? (remember the explicit IPv4 label)
  Can there be more than one entropy label in the label stack?
  Should ELIs be reserved labels? Why or why not?
  Should entropy labels be associated with tunnels or with MPLS applications?

## Slide 5: Carriers’ Carrier VPNs
CsC VPN signaling: should this include entropy label signaling or not?
End VPN signaling: transparent to CsC VPN PEs

## Slide 6: Autonomy of Carrier’s Carrier
Should the Carrier’s Carrier delegate the insertion of entropy labels to its customer?
  If customer carrier isn’t interested in entropy (they don’t have much ECMP), the Carrier’s Carrier pays the price (in bandwidth, management, etc.)
Should the Carrier’s Carrier be aware of its customer’s signaling?
Or should the Carrier’s Carrier be free to insert entropy labels if it wishes to?
Operators: take note!

## Slide 7: Autonomy
If the answer is to give the Carrier’s Carrier the freedom to insert entropy labels, then:
  There may be many entropy labels in a label stack
  This in turn means that entropy labels do not have to be at the bottom of stack
Note that applications today that assume that entropy labels are at the bottom of stack (like fat PWs or “regular” IP VPNs) are not affected

## Slide 8: Reserved ELI
Having the ELI be reserved simplifies signaling, forwarding, microcode, …
Doesn’t seem to have a downside
Should we take this to the list? To the WG chairs? To the UN?

## Slide 9: Tunnels or Apps?
ECMP is not usually associated with MPLS apps (e.g., PWs, VPNs, VPLS, …)
  ECMP is associated with MPLS tunnels
Thus, associating entropy labels with a tunnel rather than with an app seems “more right”
  It also means that we won’t need new entropy label signaling for each new app
The price, however, is to always carry an ELI …
  … unless someone has a better idea