## Slide 1: ISIS MPLS Explicit NULL Label draft-bitar-mpls-isis-explicit-null-label-00.txt
Page - <number>
Nabil Bitar (Verizon)
Himanshu Shah (Ciena)
George Swallow (Cisco)
November 2011
IETF-82, Taipei, Taiwan
Notes: <number>

## Slide 2: History
Page - <number>
RFC 4206 defines a Forwarding Adjacency (FA) with the following attributes
  An FA is a GMPLS/MPLS TE tunnel between a pair of routers
  An FA is advertised as an IGP link in the same IGP topology over which it is established
  An FA is used only for traffic forwarding – multicast is not explicitly addressed and implementations have traditionally lacked support for IP/MPLS packet replication over FAs
Routing or signaling adjacencies are never established over FAs.
  IGP topology graph is assumed to be connected via layer2 interfaces
Notes: <number>

## Slide 3: A Packet Transport Reference Model and Problem statement
Page - <number>
A GMPLS tunnel between a pair routers is signaled over a different IGP topology than that of the routers
  In contrast FAs are signaled over the same routers’ IGP topology
GMPLS TE tunnels provide the only connectivity among routers across MPLS-TP network
  In contrast, in networks where FAs are established, routers are connected over layer2 interfaces over which Routing and signaling adjacencies are formed ove
Requirement: Enable a GMPLS tunnel interface at a router head-end as a fully functional IP/MPLS interface
  Form IGP adjacencies, BGP peering sessions and multicast and MPLS signaling adjacencies over the tunnel
  Forward unicast and multicast IPv4, IPv6 and MPLS traffic over the GMPLS tunnel
<-------------- ISIS, RSVP-TE, LDP, PIM, LDP, BFD --------------->
<--------------- Tunnel LSP: Routing Adjacency ------------------>
<---Transport LSP--->
GMPLS UN GMPLS UN
+-+--+ +----+ +----+ +----+
| R1 |+----------------+| PE1|+-----------------------+|PE2 |+---------------+| R2 |
+----+ +----+ +----+ +----+
Notes: <number>

## Slide 4: Enabling a GMPLS tunnel interface as an IP/MPSL interface
GMPLS tunnel is bidirectional as any IP link
MPLS encapsulation (RFC3032) defines the encapsulation of:
  MPLS packets over MPLS tunnels
  IPv4 packets over MPLS tunnels – can be used to encapsulate user-plane packets and control plane packets (e.g., RSVP-TE, LDP, OSPF-TE, PIM)
  IPv6 packets using the IPv6 explicit NULL label (label value=2) over MPLS tunnels - can be used to encapsulate user-plane packets and control plane packets (e.g., RSVP-TE, LDP, OSPF-TE, PIM)
  any mix of MPLS and IP packets on the same MPLS tunnel – demultiplexing among encapsulated protocols is inherent to RFC 3032
Standards Gap:
  Carrying ISIS Links state Packets over MPLS is not defined – focus of the draft
Page - <number>

## Slide 5: ISIS MPLS Explicit NULL Label
Define an ISIS MPLS Explcit NULL Label to address the gap in multiplexing ISIS Link state packets, MPLS and IPv4/IPv6 unicast/multicast packets on the same GMPLS tunnel
  An enabler for supporting full IP Interfaces on GMPLS tunnels
  Similar function to the IPv6 Explicit NULL label – enable the identification of the carried protocol (ISIS) in an MPLS packet
Format of ISIS Link State packet encapsulation over a GMPLS tunnel interface enabled for ISIS
Page - <number>
+----------------------------------------------+
Tunnel label header | tunnel-label | TC| S=0| TTL |
+-----------------------------------------------+
ISIS Explicit NULL label | ISIS NULL label | TC| S=1| TTL=1 |
+-----------------------------------------------+
| |
| |
| |
| ISIS Packet |
| |
| |
+------------------------------------------------+

## Slide 6: Next Steps
Solicit WG input on the proposal
If proposal is accepted, seek the definition of an ISIS MPLS Explicit NULL label value in the reserved MPLS label space
Page - <number>