## Slide 1: LDP DoD draft-beckhaus-ldp-dod-01.txt
Thomas Beckhaus (Deutsche Telekom AG)
Bruno Decraene (France Telecom)
Kishore Tiruveedhula, Maciek Konstantynowicz (Juniper)
Luca Martini (Cisco)
IETF 82, Taipei, Taiwan

## Slide 2: draft-beckhaus-ldp-dod-01
Motivation
Updates from -00
Next steps

## Slide 3: Changes from -00
Addressed open points from Quebec and mpls list
  Updated access topologies
    Added daisy chain, horseshoes, rings, ...
  Access IGP added as alternative to static routes for subset of access topologies
  Generalized the service use cases
  Added new LDP TLV for optimized fast-up restoration
Editorial changes

## Slide 4: Motivation
Seamless MPLS design (draft-ietf-mpls-seamless-mpls) relies on LDP DoD for scalability and support of access devices
  well strutured access topologies
  compute and memory constraints limiting the amount of state access devices can hold
RFC5036 specifies LDP Downstream on Demand mode of operation
  but LDP DoD is not widely available on modern IP/MPLS devices
Goal of the draft is to address that

## Slide 5: MPLS LDP DoD in access and aggregation use cases and LDP DoD procedures
  LDP DoD session negotiation
  Label request, mapping
  Label withdraw
  Label release
  Local repair
Seamless MPLS access use cases drive the required LSR LDP DoD procedures for Access Nodes and border Aggregation Nodes
I-D.draft-beckhaus-ldp-dod-01 lists the access use cases and maps LDP DoD procedures against them
All described LDP DoD procedures rely on LDP specification [RFC 5036]
  Exception is fast-up convergence
  (AN, AGN) Initial network setup
  (AN) Service provisioning, activation
  (AN) Service changes, decommissioning
  (AN) Service failure
  (AN, AGN) Network transport failures
LDP DoD use cases (AN, AGN)
LDP DoD procedures (Access LSR)

## Slide 6: Reference access topologies with access static routes
U2
Topologies with access static routes
  I1 - a single AN homed to a single AGN
  I - multiple ANs daisy-chained to a single AGN
  V - a single AN dual-homed to two AGNs
  Y - multiple ANs daisy-chained to two AGNs
  U2 - two ANs dual-homed to two AGNs
Y
V

## Slide 7: Reference access topologies with access IGP
Y
Topologies with access IGP
  Y - multiple ANs daisy-chained to two AGNs
  U - multiple ANs in a horseshoe, dual-homed to two AGNs
U

## Slide 8: New LDP Optional Parameter TLV Queue Request
A new Optional Parameter is defined for use in the Label Request message:
Optional Parameter Length Value
Queue Request TLV 0 see below
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1|0| Queue Request (0x????) | Length (0x00) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
U-bit = 1
Unknown TLV bit is set to 1. If this optional TLV is unknown,
it should be ignored without sending "no route" notification.
Ensures backward compatibility.
F-bit = 0
Forward unknown TLV bit is set to 0. The unknown TLV is not
forwarded.
Type
Queue Request Type value to be allocated by IANA.
Length = 0x00
Specifies the length of the Value field in octets.

## Slide 9: Optimized fast-up restoration
The upstream LSR sends a Label Request message with a Queue Request TLV
  If the downstream LSR supports the Queue Request TLV
    it verifies if route is available, and replies with label mapping
    If route not available, it queues the request and replies as soon as the route becomes available; it does not send a "no route" notification back.
    upstream LSR does not retry the Label Request message if no reply from downstream LSR.
  If the downstream LSR doesn’t support the Queue Request TLV
    It replies with “no route” notification, as per current procedures.
If the upstream LSR wants to abort an outstanding label request
  The upstream LSR sends a Label Abort Request, making the downstream LSR to remove the original request from the queue and send back a notification Label Request Aborted [RFC5036].

## Slide 10: Next Steps
Comments please
MPLS WG adoption