## Slide 1: MPLS-TP Shared Mesh Protection draft-cheung-mpls-tp-mesh-protection-04
IETF 82 – Taipei, November 2011
Taesik Cheung and Jeong-Dong Ryoo (ETRI)
Yaacov Weingarten and Nurit Sprecher (NSN)
Daniel King (Old Dog)
Notes: <number>

## Slide 2: Main Points of Solution
Build on existing linear protection
  Protection switching action (re-use linear protection)
  Coordination action (defined in this draft)
One LSP for each protection path
  There is no shortage of labels
  Each LSP has end-to-end OAM/PSC channel
Parallel control of protection segments
  Minimize coordination processing time
Immediate traffic switch
  Rapid failover as fast as linear protection
Notes: <number>

## Slide 3: Principle of Operation
End node detecting failure initiates protection
  Informs Protection Switching (PS) Event to SEN
  Starts linear protection
SEN coordinates use of shared resource
  Informs Resource Allocation (RA) Notification to SSN
  Blocks low priority protection LSP and sends Lockout (LO) Request to the corresponding end node (For equal priority, waits for reply from SSN)
SSN coordinates use of shared resource
  Blocks equal or low priority protection LSP and sends LO Request (uses Protection ID for tie-break)
  Replies RA Ack to SEN
Block operation will be added in version 05.
Notes: <number>

## Slide 4: Protocol Messages
Blue: Linear protection protocol messages
Red: PS Event (EN  SEN’s)
Orange (solid): RA Notification (SEN  SSN)
Orange (dotted): RA Ack (SSN  SEN)
Green: LO Request (SEN/SSN  EN)
P
Q
R
S
T
U
C
D
E
F
G
H
A
B
Priority:
P1>P2>P3>P4
P2
P1
P3
P4
X
SF (AB)
Define another message to unblock:
LO Ack (EN  SEN/SSN)
Notes: <number>

## Slide 5: Example 1 (SF at high priority LSP)
Procedures
  A detects SF, sends PS Event to P and starts linear protection.
  P blocks P2, sends LO Request to C and RA Notification to Q.
  Q blocks P2 and sends LO Request to D (and replies RA Ack to P).
  C and D go to Lockout state.
A
P
Q
B
C
D
[ Normal ]
W1
P1
P2
W2
A
P
Q
B
C
D
[ Protection ]
X
1. SF (AB)
W1
P1
P2
W2
Priority
P1 > P2
Lockout
Lockout
Notes: <number>

## Slide 6: Example 2 (SF at low priority LSP)
Procedures
  C detects SF, sends PS Event to P and starts linear protection.
  P does nothing.
A
P
Q
B
C
D
[ Normal ]
W1
P1
P2
W2
A
P
Q
B
C
D
[ Protection ]
W1
P1
P2
W2
Priority
P1 > P2
X
1. SF (CD)
Notes: <number>

## Slide 7: Example 3 (Pre-emption)
Procedures (continued from Example 2)
  A detects SF, sends PS Event to P and starts linear protection.
  P blocks P2, sends LO Request to C and RA Notification to Q.
  Q blocks P2, sends LO Request to D (and replies RA Ack to P).
  C and D go to Lockout state. (return to the failed W2)
A
P
Q
B
C
D
[ P2 occupies P-Q ]
W1
P1
P2
W2
A
P
Q
B
C
D
[ P2 pre-empted ]
X
2. SF (AB)
W1
P1
P2
W2
Priority
P1 > P2
X
1. SF (CD)
X
1. SF (CD)
X
Lockout
Lockout
Notes: <number>

## Slide 8: Example 4 (Equal priority)
Procedures (First come, first served)
  A detects SF, sends PS Event to P and starts linear protection.
  P sends RA Notification to Q and waits for reply.
  Q blocks P2, sends LO Request to D and replies RA Ack to P.
  P blocks P2 and sends LO Request to C.
  C and D go to Lockout state.
A
P
Q
B
C
D
[ Normal ]
W1
P1
P2
W2
A
P
Q
B
C
D
[ Protection ]
X
1. SF (AB)
W1
P1
P2
W2
Priority
P1 = P2
Lockout
Lockout
Notes: <number>

## Slide 9: Example 5 (Race condition)
Procedures (Equal priority resolved by Protection path ID)
  B detects SF, sends PS Event to Q and starts linear protection.
  C detects SF, sends PS Event to P and starts linear protection.
  Q and P sends RA Notification to each other and wait for reply.
  P blocks P2, sends LO Request to C and replies RA Ack to Q.
  Q blocks P2 and sends LO Request to D.
  C and D go to Lockout state. (return to the failed W2)
A
P
Q
B
C
D
[ Simultaneous Failures ]
W1
P1
P2
W2
A
P
Q
B
C
D
[ P2 pre-empted ]
W1
P1
P2
W2
Priority
P1 = P2
(PID1 > PID2)
X
1. SF (CD)
X
1. SF (CD)
X
Lockout
Lockout
X
1. SF (AB)
X
1. SF (AB)
Notes: <number>