## Slide 1: Traffic Engineering architecture for services aware MPLS draft-fuxh-mpls-delay-loss-te-framework-02
Xihua Fu, Malcolm Betts, Qilei Wang ZTE
Vishwas Manral, Hewlett-Packard Corp.
Dave McDysan, Andrew Malis Verizon
Spencer Giacalone Thomson Reuters
John E Drake Juniper
Notes: <number>

## Slide 2: Changes since last version
Introduced at 79th,80th CCAMP and transferred to MPLS after 80th.
Refined the structure of document
Added or refined some texts to keep it consistent with following document
  draft-giacalone-ospf-te-express-path-01.txt
  draft-previdi-isis-te-metric-extensions-00.txt
  draft-fuxh-mpls-delay-loss-rsvp-te-ext-00.txt
Solved some comments from mailing-list

## Slide 3: Open Issues: Latency and jitter of Node
Advertising node latency may result in oscillation risk because of queue delay.
  Option 1: We may define it as a fixed or average/approximate latency (without any queuing) and add half of the fixed node latency to each link.
  Option 2: Assumed that the node latency is a small factor of the total latency in the networks. The node latency is hence ignored for the benefit of simplicity.
Suggestion: Queuing delay isn’t considered. Node latency can be included in the advertised link delay.
More comments from list?

## Slide 4: Open Issues: Anomalous state of link in IGP
One maximum threshold could be configured to link. If the link performance exceeds the threshold, the IGP should get the anomalous state of this link.
  Path computation entity may not select this kind of link although end-to-end performance is still met.
  The solution should support to move one end-to-end path away from any link whose performance exceeds the configured maximum threshold.
It may result in heavy configuration work.
More comments from list?

## Slide 5: Open Issues: Composite Link Performance Advertisement
Option 1: Only TLV for Composite Link. The performance may be the range, average or maximum latency/loss of all component links.
Option 2: Both a TLV for each component link, plus one for the bundle with the average.
It is related specific implementation. More comments from list?

## Slide 6: Clarification
E2E loss computation:
  1-(1-lossrate_L1)*(1-lossrate_L2)*…*(1-lossrate_Ln)
  Assume packet loss is 10% for two hops of a link. The measurements will come to 19% total packet loss. Because of 10% loss on the first link only 90% packet reach the second link where another 10% of 90% are lost, which is 9% of total packets.
There will be a little bit change in next version to clarify the e2e loss computation is multiplication of each link rather than sum.
FYI: ITU-T Y.1541

## Slide 7: Next Step
Collect feedbacks from the meeting and list
Adopt it as WG document ?