## Slide 1: MPLS-TP Shared Mesh Protection
IETF 82 – Taipei, November 2011
Authors of draft-cheung-mpls-tp-mesh-protection
Authors of draft-pan-shared-mesh-protection

## Slide 2: Solutions under Discussion
Draft-cheung-mpls-tp-mesh-protection
  Taesik Cheung and Jeong-Dong Ryoo (ETRI)
  Yaacov Weingarten and Nurit Sprecher (NSN)
  Daniel King (Old Dog)
Draft-pan-shared-mesh-protection
  Ping Pan, Rajan Rao and Biao Lu (Infinera)
  Fatai Zhang, Sam Aldrin (Huawei)
  Luyuan Fang (Cisco)
  Andrew G. Malis (Verizon)
  Fei Zhang (ZTE)
  Mohana Singamsetty (Tellabs)

## Slide 3: SMP Objectives
Sharing of protection resources
Rapid failover (optimized for packet)
Reliable message exchange
All corner cases covered
Back out on failure of protection
Notification to unprotected LSPs
Re-use of existing protection mechanisms where possible

## Slide 4: What is SMP? (Required per MPLS-TP Requirements (Req 68, 69, RFC5654))
The resources on P-Q-R are shared by multiple working LSP’s
Key properties:
  Protection LSPs’ are pre-established.
  Protection switching priority is assigned for each protection path (need to be known by shared nodes).
  Upon failure, a working LSP can be protected based on the priority.
    It may pre-empt the other LSP’s.
    Unprotected LSP’s are notified.

## Slide 5: Corner Cases to be Covered
Race condition
  P and Q receive requests from different LSP’s having same priority.
  P and Q should decide how to resolve it.
Unnecessary service interruption
  P3 and P4 should not be interrupted by P2 which will be rejected by Q.