## Slide 1: draft-koike-mpls-tp-temporal-hitless-psm-04 November 17th, 2011 Taipei
Alessandro D'Alessandro (Telecom Italia)
Manuel Paul (Deutsche Telekom)
Satoshi Ueno (NTT Communications)
Yoshinori Koike (NTT)

## Slide 2: Overview
Backgrounds and detailed requirements of new hitless and temporal path segment monitoring based on section 3.8 of RFC6371(MPLS-TP OAM framework)
Elaborates differences from Sub Path Maintenance Element (SPME)
Relevance for OAM tools:
  Intended for on-demand (temporal) OAM functions.
  In particular, mandatory for performance monitoring (LM and DM) to localize a degraded point in a transport path
Further considerations on
  Single- vs. Multi-level monitoring
  Independency from pro-active OAM functions
  Flexibility in setting of segment
Applicable in both per-node and per-interface model

## Slide 3: Updates from ver. 3
Added a new term Hitless Path Segment Monitoring (HPSM)
Added an issue in case of pre-configuration of SPMEs : Arbitrary segment monitoring is impossible
Reflected minor comments in off-line discussion

## Slide 4: Additional issue in pre-configuration of SPMEs
SPME1
Original transport path (MEP-MEP)
A
B
C
D
E
LB1=100
LB1=200
LB1=110
LB1=120
LB1=130
LB1=200
LB2=210
LB1=120
LB1=120
LB1=120
LB2=130
MEP-MEP
SPME1
MEP-MEP
SPME2
LB2=200
LB2=?
LB2=?
LB1=199
LB1=199
LB1=199
LB1=299
LB3=300
LB3=310
LB2=320
1) Nesting
2) Not nesting
SPME2
LB1=300
LB2=310
OK
NA
SPME is limited to a nesting layer stacking which restricts patterns of segment

## Slide 5: One of the possible solutions for HPSM
TTL TLV extension (draft-ietf-mpls-lsp-ping-ttl-tlv-01.txt) can be applied for HPSM
Type =TBD
Length
value
0
32
TTL value
8
16
24
A
F
E
B
C
D
Echo Request
Echo Reply
LSP
Sending OAM packet with TTL TLV option
Sending back an Echo Reply setting TTL value based on the TTL TLV information of Echo Request
(draft-ietf-mpls-lsp-ping-ttl-tlv-01.txt)
Definition of Time-to-Live TLV for LSP-Ping Mechanisms
HPSM

## Slide 6: Consideration on an event changing the TTL distance to the peer monitoring entity
Solution is out of scope of this draft, however considering it is useful to refine requirements of HPSM
In case of protection, HPSM is not required to switch from working path to protection path because working path and protection path are different.
Accordingly, TTL change is not problematic in protection SW
TTL=1
HPSM for Working transport path
Working
Protection
HPSM for Protection transport path
Automatic switching of HPSM is not required
(TTL re-discovery is not required in case of protection SW)

## Slide 7: Next steps
Solicit further comments on ver.4
Clarify the required behavior of HPSM when a protection switching occurs during its monitoring
Ask for WG poll

## Slide 8: Thank you