## Slide 1
<number>
Luyuan Fang lufang@cisco.com
Nabil Bitar nabil.bitar@verizon.com
Raymond Zhang Raymond.zhang@alcatel-lucent.com
Masahiro DAIKOKU ms-daikoku@kddi.com
Ping Pan ping@pingpan.org
November 17, 2011
IETF 82, Taipei, Taiwan

## Slide 2: Contributing co-authors
<number>
Luyuan Fang
Nabil Bitar
Raymond Zhang
Masahiro DAIKOKU
Ping Pan
Dan Frost
Jianping Zhang
Mach Chen
Lei Wang
Nurit Sprecher
Henry Yu

## Slide 3: Objective and Status
Objectives:
  Provide MPLS-TP use case studies
  Discuss design considerations and options
  Intent to serve as best practice guide
Status
  Issued 04 version
    Complete use case scenarios
    Additions to reflect recent development experience
    Point to draft-martinotti-mpls-tp-interworking-02.txt for interworking
  Adopted as MPLS WG document 11/17/2011
    Thanks for the support of WG and comments by many folks!
  Will first update to WG document without any other change
  The will change the document title to “MPLS-TP Applicability; Use Cases and Design” and upload again
    Agreed with Eric Gray suggestion through WG poll.
    Following Chairs recommendation on change process.
<number>

## Slide 4
<number>
Use cases
  Metro Agg/Acc, Packet Optical Transport, Mobile backhaul
  MPLS-TP provides the transport for multi-services, e.g. wireline/wireless, business VPNs/residential broadband, whole sale/retail…
  Bring in latest real world deployment/planning examples which using IETF standards MPLS-TP solutions.

## Slide 5: Unified MPLS
Access
MPLS
Business
Corporate
Residential
STB
Access
Metro Aggregation
Core
Any Access Technology Mapped into MPLS-TP
Legacy
Utility
IP/MPLS Core and Service Edge
End to End Management
RBS
Pre-Aggregation
IP/MPLS
Core
Multi-Service Edge
RBS
Packet Transport Aggregation
MPLS-TP Aggregation
Unified MPLS
MPLS-TP Pre-agg
Pre-Agg
Ethernet

## Slide 6
MPLS-TP over WDM Ring
Upto 100G IPoDWDM
Muti-Service Edge
Aggregation Node
Core router
Access Node
MPLS-TP Access Ring
MPLS Core & Service Edge
MPLS-TP
Agg. & Access
City Y
MPLS-TP Metro
City Z
MPLS-TP Metro
City X
MPLS-TP Metro
Use Case 1: MPLS-TP For Metro Aggregation and Access
(Most common)

## Slide 7
Use Case 2: MPLS-TP For Optical Packet Transport
Core
WDM
MPLS-TP
MPLS-TP
MPLS-TP
WDM
WDM
IP/MPLS
Ethernet
IP or MPLS
MPLS-TP
MPLS-TP
IP/MPLS
Ethernet
Aggregation
Aggregation
Access
Access
Server Layer - Optical Packet Transport
Client Layer – Support L2/L3 Service

## Slide 8
<number>
Working LSP
PE
PE
Protect LSP
Dynamic Control Plane:
GMPLS for LSP
tLDP for PW
Client node
Client node
Dynamic MPLS-TP LSP
Pseudowire
Client Signal
Dynamic control plane provisioned working path and protect path
MPLS-TP in-band OAM: BFD CC/CV, AIS/RDI/LDI
Transport Tunnel 1:1, 1+1, 1:N protection, switching triggered by in-band OAM
Preferred option - if Operation Model allows
MPLS-TP with Dynamic Control Plane
GMPLS:
  RSVP-TE
  OSPF-TE/ISIS-TE

## Slide 9
<number>
Design Considerations – when to use MPLS-TP?
When to consider MPLS-TP?
  Most common use case: replacing SONET/SDH with MPLS-TP
  Typical applications:
    Metro aggregation access
    Mobile back-haul
    Long-haul optical packet transport
Which MPLS-TP Model?
  Depending on the operational model and long term planning
    Dynamic with GMPLS control plane is preferred if ops model allows
    Static provisioning model may provide easy adaption for the transport ops – most commonly adopted practice today
Can MPLS-TP be used to replace IP/MPLS?
  No. MPLS-TP is MPLS focused on transport-only features, it does not provide L2/L3 services functions as IP/MPLS does

## Slide 10: More on General Design Considerations
  Protection
    1:1, 1+1, 1:N (1 protects n working lsps)
    Linear/Ring/Shared mesh protection
    Recovery coordination among layers
    PW protection and LSP protection
    Support of multi-homing, multi-chassis redundancy
    Delay variation between working and protect LSPs
  OAM
    Balance between protection coverage and efficiency/reduce complexity
    Tuning BFD hello interval and hold off timer
    Distance impact to AIS/RDI/LDI – use of TP style fast reroute
    Clocking and loss/delay measurement
    Use of loopback and lock Instruct for test and maintenance
    OAM and control plane relations

## Slide 11
MPLS-TP PW Design Considerations
Does PW work the same as in IP/MPLS?
  Mostly yes.
    Both SS-PW and MS-PW are supported
    tLDP is used for dynamic control plane
  PW status is new OAM feature for failure notification for static provisioning
  Both directions of a PW must be bound to the same transport bidirectional LSP
When multi-tier rings involved, should S-PE be used or not?
  Pros for using S-PE
    Domain isolation, may facilitate trouble shooting
    the PW failure recovery may be quicker
  Cons for using S-PE
    Adds more complexity
    If the operation simplicity is the high priority, some SPs choose not to use S-PE, simply forming longer path across primary and secondary rings.
Should PW protection be used in addition to LSP protection?
  An operator choice. Pros for using PW protection
    PW is protected when both working and protect LSPs carrying the working PW fails as long as the protection PW is following a diverse LSP path from the one carrying the working PW
    Adds more complexity, some choose not to use.

## Slide 12
Working PW is configured over LSP Green tunnel interface with working and protect paths.
When LSP Green working path fails, it switches to lsp Green Protect. No PW switching is needed.
PW protection takes place only when both lsp Green Working and Protect paths fail, PW will switch to the protect PW which is attached on the lsp Red tunnel int.
PW protection is set to protect from LSP failures on both working and protect
LSP Green Working
LSP Red Working
LSP Red Protect
LSP Green Protect
Protect PW over LSP Red
Working PW over LSP Green
LSP tunnel interface
PW Protection
Notes: <number>
<number>

## Slide 13
Proactive and Event Driven MPLS-TP OAM Tools
Should both proactive fault detection and event driven tools be used ?
  Yes
  LDI is event driven
    Fiber cut will cause LDI message generated and trigger immediate protection switching.
  BFD hello is used for proactive fault management
    BFD sessions should be configured for both working and protecting LSPs
    BFD hardware support for scalability
    No dependency on Control Plane or Management Plane
Unidirectional Failure
  When Unidirectional failure happen, RDI will send the failure notification to the opposite direction to trigger both end switch over.

## Slide 14: Next Steps
<number>
More input/comments from WGs appreciated – especially based on design/deployment experience.