## Slide 1: MPLS-TP TE MIB
draft-ietf-mpls-tp-te-mib-00.txt
Sam Aldrin
Tom Nadeau
Venkatesan Mahalingam
Kannan Sampath

## Slide 2: Motivation
  The existing MPLS TE [RFC3812] and GMPLS MIBs [RFC4802] do not support the transport network requirements of NON-IP based management and static bidirectional tunnels.

## Slide 3: MPLS TP extensions to TE MIB
  MPLS Tunnel Table in MPLS-TE-STB-MIB is used for MPLS TP tunnels as well
  MPLS Node Configuration Table is being added to map Global ID and Node ID combination and/or ICC identifier for Ingress and Egress LSR’s
  A local number generated for the combination, will be used to index into MPLS Tunnel Table.
  MPLS Tunnel Table is augmented to support MPLS TP specific objects

## Slide 4: Updates
  The MIB definitions of Textual Conventions, Identifiers and LSR extensions are retained in MPLS-TP TE MIB draft for easy maintenance.
  Comments are received for making the MPLS-TP TE MIB as read-only MIB

## Slide 5: Additional MPLS TP MIBs We Are Working On
To support MPLS TP OAM requirements, more MIBS are being added and will appear after the IETF meeting:
  MPLS TP Protection Schemes (LPS, RPS and MPS) support using MIB
  MPLS Loss and Delay measurements using MIB

## Slide 6: Next Steps
  Conclusion on read-only MIB
  Last Call will be requested

## Slide 7: Thank You