## Slide 1: BFD MIB Extensions for MPLS and MPLS-TP Networks
draft-vkst-bfd-mpls-mib-00
Sam Aldrin
Tom Nadeau
Venkatesan Mahalingam
Mukund Mani
Kannan KV Sampath

## Slide 2: Motivation
  The existing BFD MIB [draft-ietf-bfd-mib-10] models the BFD protocol functionality to support neighbor monitoring in IP networks. It does not support the requirements for usage of BFD over MPLS and MPLS-TP networks

## Slide 3: Introduction
  This draft defines extensions to the BFD-STD-MIB to configure BFD for MPLS and MPLS-TP paths
  Objects described in the MIB will support the functionalities for BFD over MPLS [RFC 5884] and Proactive CC-CV-RDI for MPLS-TP using BFD [draft-ietf-mpls-tp-cc-cv-rdi-06]
  The MIB defines the following
    Extensions to BFD Session table
    Extensions to BFD Session Performance table

## Slide 4: BFD MIB Extensions
  BFD Session Extension Table
    Objects defined to identify BFD session parameters catering to MPLS/MPLS-TP networks
      Session Role (Active/Passive)
      Session Mode (CC/CV)
      Timer Negotiation Flag – To enable/disable timer negotiation
    Objects to associate the BFD session to the MPLS or MPLS-TP paths
      Map Type – To specify the type of path being monitored (Non-TE LSP / TE LSP / PW / MEP)
      Map pointer – Row pointer to associate the BFD session to the respective instance of the path being monitored
  BFD Session Performance Table Extensions
    Performance counters for Mis-connectivity defects, Loss of Continuity defects, Remote Defect Indications

## Slide 5: Usage of existing object bfdSessType
  Existing value “multiHopOutOfBandSignaling” of the object bfdSessType in BFD-STD-MIB will be used to identify OOB bootstrap mechanism for BFD session

## Slide 6: Example
3
Map Type
mplsTunnelName.100.1.10.20
True
1
1
1
Map Pointer
Timer Negotiate
Session Mode
Session Role
BFD Session Index
Tunnel1
MPLS Tunnel Name
20
10
1
100
Egress LSR Id
Ingress LSR Id
Tunnel Instance
Tunnel Index
Standard MPLS Tunnel Table
BFD Session Extension Table
Example: BFD Session for MPLS TE tunnel

## Slide 7: Next Steps
  Does the WG find this work useful and satisfying for the chartered items towards BFD MIB module for MPLS and MPLS-TP networks?
    If so, we ask that the WG accept draft-vkst-bfd-mpls-mib-00 as WG document
  Additional comments/reviews are requested

## Slide 8
Thank You