## Slide 1: Requirements and Framework for Unified MPLS Sub-Network Interconnection draft-allan-unified-mpls-req-frmwk-00
Dave Allan
david.i.allan@ericsson.com

## Slide 2: Background
Starting point was “Interworking between MPLS-TP and IP/MPLS”
  draft-martinotti-mpls-tp-interworking
We realized it was a prime, but not the only practical example of “FOO to BAR” interworking in the MPLS space
  “FOO to FOO” had been previously explored
    E.g. IP/MPLS Forum M-ICI
It would make sense to generalize mechanisms to support “FOO to BAR” interworking scenarios to maximize utility

## Slide 3
Problem Space
MPLS has numerous operating models or “profiles” that can be interconnected or stacked
  infrastructure: topology driven, traffic engineered, transport
  services: VPLS, VPWS, BGP L3 VPN, BGP MPLS VPN
  Both with a variety of control plane/management plane options
Stacking MPLS has typically seen a logical decoupling of the layers
  Minimizes operational impacts and permits “separation of interest” between infrastructure, operations and services
    For example: overlaying BGP VPN on hop-by-hop LDP just “works”
    This has permitted process “re-engineering” by operators
What has been missing to date is the same logical decoupling and “separation of interests” for peer interconnect
This is what the Sub-Network Interconnect draft sets out to address

## Slide 4
Content of the Draft
The draft lays out a framework and requirements to permit definition of the “meta rules” for mapping connectivity in one sub-network to another sub-network at a particular label level
  Abstracted to the level of how LSPs are identified in automation
    Connect this domain “A” LSP to this domain “B” LSP
    This will ultimately resolve down to label mappings at a border node
What is required is a generalized object that permits any MPLS LSP/PW description to be mapped to any other description
  And the object will have a number of attributes independent of the sub-networks that are interconnected
And the overall solution will have a number of requirements
  Migration to a common set of OAM DP identifiers/encapsulations
    This is enabled by the MPLS-TP work
  Desirable operational characteristics
    Hitless adds/moves/changes
  Persistency
    logical binding is independent of the state of the LSP in each domain

## Slide 5
Border node
Border link (effectively two border nodes back to back, with a one-hop sub-network between them)
Sub-network “B”
Scenarios As per draft-martinotti
Sub-network “A”
CP/MP IWF
ILM
NHLFE
ILM
NHLFE
Sub-network “B”
Sub-network “A”
CP/MP IWF
ILM
NHLFE
ILM
NHLFE
CP/MP IWF
ILM
NHLFE
ILM
NHLFE

## Slide 6: Next Steps
Collect comments
  Explicitly seeking WG feedback!
    Have we identified all the issues?
Identify gaps in current work to produce a “complete solution”