## Slide 1: 82nd IETF - Taipei, Taiwan
IJ. Wijnands ice@cisco.com
P. Hitchen paul.hitchen@bt.com
N. Leymann n.leymann@telekom.de
W. Henderickx wim.henderickx@alcatel-lucent.com
draft-wijnands-mpls-mldp-vpn-in-band-signaling-00
Notes: <number>

## Slide 2: Problem we’re solving
draft-ietf-mpls-mldp-in-band-signaling-04, documents a solution to map (1:1) Multicast Source trees (S,G) to mLDP LSPs.
This is documented for the sources that are in the global table context, no VRF.
The assumption at the time was that this is mostly used for IPTV like deployment which is in global table context.

## Slide 3: Problem we’re solving (cont)
Some providers use specific, dedicated VRF’s to transport IPTV content across the network.
The applicability of a simple 1:1 mapping of multicast Source trees to mLDP LSPs applies here as well.
This draft documents the procedures needed to transport Multicast sources trees in a VRF context over mLDP LSPs via in-band signaling.

## Slide 4: Solution
Multicast tree information, like (S,G) or (*/M,G) is encoded in the opaque field of the mLDP FEC by the egress router(s).
Including the RD of the Source (or RP) as advertised by BGP.
The mLDP LSP is build through the MPLS core with (S,G,RD), or (*/M,G,RD).
This follows a similar approach as the VPN-recursive opaque encoding in: draft-ietf-mpls-mldp-recurs-fec-04

## Slide 5: Solution (cont)
By adding the RD we’re making the LSP unique in the core network.
This prevents overlapping addresses.
Each VPN IP multicast flow creates a unique LSP in the core.

## Slide 6: Opaque encodings
We defined 4 new opaque encodings:
Transit VPNv4 Source TLV
Transit VPNv6 Source TLV
Transit VPNv4 Bidir TLV
Transit VPNv6 Bidir TLV

## Slide 7: Transit VPNv4 Source TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Source
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Group
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Route Distinguisher |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Type: (to be assigned by IANA).
Length:16
Source: IPv4 multicast source address, 4 octets.
Group: IPv4 multicast group address, 4 octets.
RD: Route Distinguisher, 8 octets.

## Slide 8: Transit VPNv6 Source TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Source ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ | Group
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ | ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Route Distinguisher |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Type: (to be assigned by IANA).
Length:40
Source: IPv6 multicast source address, 16 octets.
Group: IPv6 multicast group address, 16 octets.
RD: Route Distinguisher, 8 octets.

## Slide 9: Transit VPNv4 bidir TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Mask Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RP |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Group |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Route Distinguisher ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Type: (to be assigned by IANA).
Length:17
Mask Length: Length of the mask for group address, 1 octet.
RP: IPv4 multicast address, 4 octets.
Group: IPv4 multicast group address, 4 octets.
RD: Route Distinguisher, 8 octets.

## Slide 10: Transit VPNv6 bidir TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Mask Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ RP ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Group ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Route Distinguisher ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Type: (to be assigned by IANA).
Length:41
Mask Length: Length of the mask for group address, 1 octet.
RP: IPv6 multicast address, 16 octets.
Group: IPv6 multicast group address, 16 octets.
RD: Route Distinguisher, 8 octets.

## Slide 11: Scalability
Each IP multicast flow maps to a LSP.
Works well if the number of multicast flows is under control by the operator.
mLDP is receiver driven, so its expected to scale well for thousands of LSPs.
Scalability consideration is the same for both global table and VPN sourced multicast trees.

## Slide 12: Applicability
This solution is NOT intended to be used as general purpose MVPN, like in; draft-ietf-l3vpn-2547bis-mcast-10
It is a specific use-case where VRF’s just happen to be used for transporting IPTV like multicast traffic.
Don’t panic.

## Slide 13: L3VPN
This draft does describe minimal L3VPN specific procedures, the use of RD.
draft-ietf-mpls-mldp-recurs-fec-04, does exactly the same.
I propose to follow the same path as done for recurs-fec, do the work in MPLS WG, potentially do an last-call in L3VPN WG.

## Slide 14: Going forward
Authors like to get comments on the draft.
The intention is to make this a WG document.

## Slide 15: Questions?